## Slide 1: Digital Control and Automatic Control
Instructor: Sanghyuk Lee
Sanghyuk.Lee@xjtlu.edu.cn
Tel: 8816-1415
Department of Electrical and Electronic Engineering
XJTLU

## Slide 2: Digital Control and Automatic Control EEE327
Module Code: EEE327
Originating Department: Electrical & Electronic Engineering
Module Level: Level 4
Module Credit: 2.5
Instructor: Sanghyuk Lee
Sanghyuk.Lee@xjtlu.edu.cn
Tel: 8816-1415

## Slide 3
AIM of Module:
To familiarize control theory, signal flows, simulation tools
To equip knowledge of analysis and design of automatic control systems(Continuous/Discrete system)
Learning Outcomes:
A better understanding of linear systems
An ability to develop system models, and use them to design feedback control laws to stabilize system
Good understanding of how to control continuous systems via digital controller
Digital Control and Automatic Control EEE327

## Slide 4: Digital Control and Automatic Control EEE327
Method of Teaching and Learning:
Formal Lecture (1.5 hrs./week)
Tutorials-Problem solving in lecture hour (2 times)
Q&A in Office times (2-4 pm/Mon. 9-11 am/Thu.)
Assessment:
Final Exam-70%, Midterm Exam-15%
Two times Assignments-15%

## Slide 5
Essential texts:
    Modern Control Systems, Richard C. Dorf, Robert H. Bishop, Pearson
References:
  Feedback Control of Dynamic Systems, G.F. Franklin, J.D. Powell, Abbas E-N, 6th ed.
  Automatic Control Systems, B.C. Kuo
  Modern Control Engineering, K. Ogata
Teaching Material:
  Lecture Notes by Instructor
Digital Control and Automatic Control EEE327

## Slide 6
Brief Syllabus(1):
Overview and Feedback Control(1 week)
Review/Dynamic models & system(1 week)
Review/Feedback stability & Root Locus(2 weeks)
Fuzzy control method(2 weeks)
  One time Assignment is planned
  Mid Exam is planned (Week 7)
Digital Control and Automatic Control EEE327

## Slide 7: Digital Control and Automatic Control EEE327
Brief Syllabus(2):
Frequency response design(1 week)
State space controller design(2 weeks)
Digital controller design(2 weeks)
Control system: Case study(1 week)
  One time Assignment is planned
  Final Exam

## Slide 8: Figure 1.1 (a) Component block diagram of a room temperature control system; (b) plot of room temperature and furnace action
Digital Control and Automatic Control EEE327

## Slide 9: Figure 1.3 Component block diagram of automobile cruise control
Digital Control and Automatic Control EEE327
How to design controller ?
  Time Domain
  Frequency domain
What’s the control objective ?
  sense
  criteria
Methods ?
  PID/ Adaptive/Robust/Optimal/fuzzy

## Slide 10
Figure 1.5 Open-loop cruise control
Analysis: for r = 65 and w = 0, there is no error
when w = 1%, then y = 60, it results 7.69% error speed
Typical example of open loop system
  It has the weak point over exterior disturbance
  Need to adjust input variable u by comparison with output y
Digital Control and Automatic Control EEE327

## Slide 11: Figure 1.6 Closed-loop cruise control
Large loop gain over open loop control structure
Digital Control and Automatic Control EEE327
Combining them,
Feedback reduces the sensitivity of speed error
Comparison with open loop system
  Let
It is obvious that much better against open loop system(7.69% error speed)
It means “Robust to the disturbance” and “Food performance” by the point of output
However, it invokes also unstable system(later work)
Hot Issue : To get the gain as large as possible to reduce the errors without the system unstable

## Slide 12: Figure 1.7 Early historical control of liquid level and flow
Previous Control System Examples (1)
System Object: maintain water flow properly
System Controller: Float
Source: Water supply from outside
Is this System open loop or closed loop ?
What is sensor?
What is actuator?
What is system output ?
Digital Control and Automatic Control EEE327

## Slide 13: Figure 1.8 Drebbel’s incubator for hatching chicken eggs Source: Adapted from Mayr, 1970
Previous Control System Examples (2)
System Object: maintain temperature to incubate eggs
System Controller: Damper
Source: Flue gas heat from fire
Is this System open loop or closed loop ?
What is sensor? Alcohol(expand/contract)
What is actuator? Damper/riser/float
Digital Control and Automatic Control EEE327

## Slide 14: Figure 1.10 Close-up of the fly-ball governor Source: British Crown Copyright, Science Museum, London
Figure 1.11 Operating parts of a fly-ball governor
Previous Control System Examples (3)
Is this System open loop or closed loop ?
What is sensor? Ball angle
What is actuator? Lever to open main valve
1st Load change
2nd Speed variation make ball angle change
3rd Sleeve --> lever
4th Steam flow change
Digital Control and Automatic Control EEE327

## Slide 15
Surveys of Control Theory
At first, control system was designed through just experience not theoretical point of view
Later, G.B Airy(1820s to 1840s): discuss instability in a feedback system using differential eq.
Stability Analysis
  J.C. Maxwell(1868) stated that stability depends on the roots of characteristic equation
  R.E Routh(1877) introduced stability criterion with simple technique
  A.M. Lyapunov(1893) studied stability of motion which was based on nonlinear differential eq.
Frequency Response
Problem of amplifier(need many amplifier for long distance telephoning)
It needed feedback structure(less error)
Except high gain, higher dimension problem
Solved by Nyquist(1932) and Bode(1945)
PID Control
Callender et al (1936) described first
Based on experimental work
Proper for process having relatively long time delay between actuator and sensor
Applicable not only complex but also nonlinear
As a result, very popular
Root locus
W.R Evans(1948) developed techniques and rules to follow the paths of roots of the characteristic eq.
Suitable for design, stability analysis
State variable/Modern control
Bellman, Kalman and Pontryagin(1950s) began again to consider ODE which was stimulated by the control of earth satellites
Optimal control(Wiener and Phillips during World War 2)
This method use ODE directly not use
frequency response or characteristic eq.
Digital Control and Automatic Control EEE327

## Slide 16
Process of designing control system
Study the system controlled: Decide sensors, actuators, etc.
Modelling the system : Time domain, Frequency domain, state space approach, etc.
What is sensor, and actuator ?
Modelling process
Start from Newtonian Equation
Rectangular equation from polar cordinate
Derivate two times and express it by angular and length directional acceleration
By newton’s 2nd law
Figure 2 pendulum
Digital Control and Automatic Control EEE327

## Slide 17
Process of designing control system
Simply the model if necessary
Analyze the resulting model
First equation is not needed because is constant.
Also is the same to because of gravity.
Make the model in Fig. 2 simple, then
It also approximated by by taylor series expansion
Next, state space expression and frequency domain expression is followed.
Digital Control and Automatic Control EEE327

## Slide 18
Process of designing control system
Decide on the type of controller to be used
Design a controller to meet the spec.
Simulate the resulting controlled system: on computer simulation or pilot plant
From state space expression and frequency domain expression, controller is proposed such as
PID, Optimal, Adaptive, Robust, Intelligent, etc..
Check the specification, whether it is satisfied or not.(Simulation/Experiment)
Choose hardware and software and implement the controller
Tune the controller on-line if necessary
Digital Control and Automatic Control EEE327

## Slide 19: Digital Control and Automatic Control
End of Lecture 1