## Slide 1: Electronic Circuits and Systems EEE211
How Diodes Work - Review
Dept. of Electrical & Electronic Engineering
XJTLU

## Slide 2
Part 1: Diode

## Slide 3: Electronic Circuits and Systems EEE211
Silicon is by far the most common semiconductor material used to make transistors. There are some other semiconductor materials used, but only for very special purposes (e.g. for use at microwave frequencies).
To understand how semiconductor devices work it is first necessary to be familiar with the electrical behaviour of semiconductor materials.
Silicon has gained this lead because its basic properties are well suited for most transistor applications and because of the large amount of research and development work undertaken on this material over the years – in particular it is possible to grow a very good quality oxide on its surface (which is an excellent insulator), and the silicon itself can be made with very high quality – i.e. free of defects and unintended impurities.
How Diodes and Transistors work (review)

## Slide 4: Electronic Circuits and Systems EEE211
‘Intrinsic’ semiconductors
Electron energy
Conduction band
Valence band
-
+
Distance
Free electrons move in the conduction band and represent a negative charge
Free holes move in the valence band and represent a positive charge
Free electrons can be created thermally by liberating an electron from the crystal covalent bonding scheme
This also creates a hole that is able to move and, like the electron, conduct electricity
Si
Si
Si
Si
Si
Si
Si
Si
Si
-
+
Free hole
Free electron
In an intrinsic semiconductor, the electrons and holes will exist in equal numbers.

## Slide 5: Electronic Circuits and Systems EEE211
‘Extrinsic’ semiconductors
An N-type extrinsic semiconductor is made by adding donor impurities (i.e. valence 5 atoms) in controlled numbers into the pure (intrinsic) silicon. These take the place of a silicon atom in the crystal and are therefore known as ‘substitutional’ impurities.
P+
Si
Si
Si
Si
Si
Si
Si
Si
-
For example, if a known quantity of phosphorous atoms (valence 5) are introduced into the silicon lattice, each phosphorous atom can take the place of one silicon atom.
Only four of the five valence electrons from each phosphorous atom are needed to satisfy the covalent bonding of the crystal.
The remaining electron is free to move in the semiconductor, leaving a positive charge on the fixed phosphorous atom.

## Slide 6: Electronic Circuits and Systems EEE211
Relatively little energy is required to separate the spare electron from its parent phosphorous atom (0.045eV compared with the average thermal energy of 0.025eV). At normal operating temperatures, almost all the phosphorous atoms will have been separated from their spare electron.
This is n-type material.
Electron energy
Conduction band
Valence band
Distance
-
+
-
+
-
+
-
+
-
+
Note that the free electron has been introduced without a corresponding hole in the valence band – so the density of electrons will now be higher than the density of holes.
However, note that the material is still electrically neutral because n = p + ND

## Slide 7: Electronic Circuits and Systems EEE211
e.g. boron
B-
Si
Si
Si
Si
Si
Si
Si
Si
This time, there are only three valence electrons available to satisfy the covalent bonding of the crystal. This effectively introduces a ‘hole’ (i.e. an empty valence state) into the semiconductor
The hole is free to move (in the same way as a hole was able to move in an intrinsic semiconductor), leaving a negative charge on the fixed boron atom.
Alternatively, a P-type extrinsic semiconductor is made by adding acceptor impurities (i.e. valence 3 atoms) in controlled numbers into the pure (intrinsic) silicon. These also become ‘substitutional’ impurities.

## Slide 8: Electronic Circuits and Systems EEE211
A small amount of energy will be required to move a valence electron from a neighbouring silicon atom into the vicinity of the boron atom. The energy is small however and is easily available thermally (0.045eV compared with the average thermal energy of 0.025eV). When this happens, the boron atom may be considered to have released its previously bound hole into the valence band.
At room temperature, almost all the boron atoms will have accepted an electron from the valence band and therefore their previously bound hole is free to move in the valence band.
This is p-type material.
Electron energy
Conduction band
Valence band
Distance
+
-
-
+
+
-
+
-
+
-
+
-
This time, the density of holes will be higher than the density of electrons.
The material is still electrically neutral because p = n + NA

## Slide 9: Electronic Circuits and Systems EEE211
The Table below shows the activation energies (in eV) of common dopant impurities.
 | Impurity | Silicon | Germanium
P-type | Boron | 0.045 | 0.010
 | Aluminium | 0.057 | 0.010
 | Gallium | 0.065 | 0.011
 | Indium | 0.16 | 0.011
N-type | Phosphorous | 0.045 | 0.012
 | Arsenic | 0.049 | 0.013
 | Antimonide | 0.039 | 0.010

## Slide 10: Electronic Circuits and Systems EEE211
The semiconductor pn junction diode
Diodes are often made by starting with n-type silicon and adding boron in well defined regions – hence creating a pn junction.
Thin wafer of n-type silicon with polished top surface
Thin (m) oxide grown on top surface
Hole etched through oxide
N-type
N-type
N-type
Boron diffusion
Aluminium metallisation
Electrical contacts added top and bottom
N-type
P-type
N-type
P-type
N-type
P-type

## Slide 11: Electronic Circuits and Systems EEE211
What happens when n and p type semiconductors are brought into electrical contact?
When in electrical contact, the large number of electrons in the n-type material are able to flow into the p-type region
Likewise the large number of holes in the p-type flow into the n-type region
This transfer of electrons and holes causes the n-type to become positive with respect to the p-type material – a contact potential is created
Electron energy
CB
VB
-
+
+
-
-
-
-
-
-
-
-
-
+
+
+
+
-
+
+
+
+
+
+
+
+
P-type
N-type
-
-
-
-

## Slide 12: Electronic Circuits and Systems EEE211
This flow of charge ends when the contact potential becomes just sufficient to prevent any further flow of electrons and holes.
Electron energy
CB
VB
-
-
+
+
-
-
-
-
-
-
-
-
+
+
+
+
+
+
+
+
P-type
N-type
-
-
-
-
+
+
+
+
Note:
The n-type side is positive with respect to the p-type side. It appears lower down on this diagram because electron energy is qV where q is the electronic charge, which is negative.
(-1.609x10-19 coulombs)

## Slide 13: Electronic Circuits and Systems EEE211
Note that the contact potential cannot be measured directly because there are equal and opposite contact potentials created at the contacts.
pn junction contact potential
contact potential at contact to n-type
contact potential at contact to p-type
V = 0
UNLESS – the temperature of the contacts becomes different from that of the junction – this changes one of the local contact potentials and a voltage is then measured - thermoelectric effect

## Slide 14: Electronic Circuits and Systems EEE211
What happens at the pn interface when a forward voltage is applied - i.e. when the p-type side is made positive relative to the n-type side?
The pn junction under forward bias
The applied voltage reduces the barrier height and electrons in the n-type material are able to flow into the p-type region
Likewise holes in the p-type flow into the n-type region
+
Because of the energy distribution of the electrons and holes, the current increases exponentially with the applied bias
Electron energy
CB
VB
-
+
-
-
-
-
-
-
-
-
-
+
+
+
+
+
+
+
P-type
N-type
-
-
-
-
+
+
+
+
+
+
-
-
-
-
-
-
+
+
+
+
+
-

## Slide 15: Electronic Circuits and Systems EEE211
If the polarity of the applied voltage is reversed, the barrier is made larger
The pn junction under reverse bias
The increased barrier height prevents electrons and holes crossing the junction except for a small number of electrons in the p-type material and holes in the n-type region. These are called minority carriers
The flow of minority carriers causes a small temperature dependant ‘leakage’ current to flow in reverse bias
Electron energy
CB
VB
-
+
-
-
-
-
-
-
-
-
-
+
+
+
+
+
+
+
P-type
N-type
-
-
-
-
+
+
+
+
+
+
+
-
-
-
-
-
-
+
+
+
+

## Slide 16: Electronic Circuits and Systems EEE211
The electrical characteristics for the diode are therefore:
Diode current (mA) (linear scale)
Applied diode voltage, VD (linear scale)
Vγ
Very small ‘leakage’ current (typ ~nA)
Rapid increase in current when VD = Vγ

## Slide 17: Electronic Circuits and Systems EEE211
A detailed analysis of the electron and hole currents that flow in the diode support the experimentally verified diode equation:
The diode has a very non-linear characteristic
– not like a resistor.
So how do we analyse circuits that have diodes in them?
REMEMBER THIS EQUATION
Diode current (logarithmic scale)
Applied diode voltage, VD (linear scale)
Vγ
Exponential increase in current
n = 2
n = 2
n = 1

## Slide 18: Electronic Circuits and Systems EEE211
Compare the real diode characteristic with an approximate ‘straight line’ characteristic
ID
VD
Vγ
Neglect leakage
Approximate with a straight line, slope 1/Rd
‘Turn-on’ voltage
Typical values for Vγ
(N.B. varies with diode size and temp):
Material turn-on voltage
Ge 0.3
Si 0.7
GaAs 1.1
GaAsP 2.1
Rd is usually a few ohms (often neglected)
In most electronic circuits, it is sufficiently accurate to replace the diode with an equivalent circuit made up from linear components, that reproduces the actual electrical characteristic of the diode.
NB we may need to be careful not to use the equivalent circuit model if high accuracy is required or the circuit is conducting either very low or very high currents. In these cases a computer analysis using (for example) Pspice will be needed.

## Slide 19: Electronic Circuits and Systems EEE211
To create the equivalent circuit, we represent the real diode as a perfect diode but with added circuit components that take into account the differences between the characteristics of the real diode and a perfect diode. This is known as a ‘piece-wise linear’ equivalent circuit model of the diode.
ID
VD
Vγ
Neglect leakage
Approximate with a straight line, slope 1/Rd
‘Turn-on’ voltage
P
N
=
=
(real)
(ideal)
Rd
Vγ
Actual diode characteristic
Equivalent circuit diode characteristic
Ideal diode characteristic

## Slide 20: Electronic Circuits and Systems EEE211
where Is = 1e-14 amps and RS = a ‘parasitic’ series resistance = 20 ohms
Plotting this characteristic gives:
RD = 1/slope = 25ohms
(note RD is slightly more than RS because of the finite slope of the exponential diode characteristic)
Vg = 0.67 volts
Fitting a straight line to the characteristic gives Vg = 0.67 volts and RD = 25 ohms
Example
We will analyse a diode circuit using a piece-wise linear approximation to the true diode characteristic.
Suppose the diode characteristic is given by:

## Slide 21: Electronic Circuits and Systems EEE211
(ideal diode)
RD
Vγ
Real diode
1k
5v
Now consider the following diode circuit and solve it using a piecewise linear approximation for the diode.
Sum the voltages around the circuit :
Now compare with more accurate answer using the previous piece wise linear model with RD = 25 ohms and Vg = 0.67 volts
First approximation assuming RD ~ 0 and Vg ~ 0.7 volts
5 – I x 1000 – 0.7 = 0
I = 4.3 mA
I = 4.224 mA
Conclusion – the accuracy of the piecewise model is often good enough for most applications and allows quick estimates to be made in simple circuits.
Use PSpice if greater accuracy is necessary or if the circuit is complex.
Finally compare with accurate (computer) solution:
I = 4.223 mA

## Slide 22
Part 2: Exercise on Diodes

## Slide 25
TYU 1.11
The power supply (input) voltage in the circuit of Figure is and the diode cut-in voltage is
(assume forward diode resistance ). The power dissipated in the diode is to be no more than .
Determine the maximum diode
current and the minimum value of to meet the power specification.
DC Analysis

## Slide 26: Electronic Circuits and Systems EEE211

## Slide 27
AC Analysis
Figure: Diode circuit with combined DC and sinusoidal input voltages

## Slide 28
AC Analysis

## Slide 29
AC Analysis

## Slide 30
AC Analysis

## Slide 31
AC Analysis

## Slide 32
AC Analysis

## Slide 33
AC Analysis

## Slide 34
AC Analysis

## Slide 35
AC Analysis

## Slide 36: Electronic Circuits and Systems EEE211
See Page 57 in Neamen’s textbook (4th edition) for more exercise.