## Slide 1: Electronic Circuits and Systems EEE211
How BJTs Work
- Review
Dept. of Electrical & Electronic Engineering
XJTLU

## Slide 2
Part 1: Bipolar Junction Transistor

## Slide 3: Electronic Circuits and Systems EEE211
Bipolar – this was the first type of transistor to be developed after its principle was discovered (accidentally!) in 1948. They are still widely used because of their high gain properties.
MOS – these transistors are a later development and are very popular because of the ease with which they can be integrated to produce I.C’s with high transistor packing density.
Transistors
There are two ‘families’ of transistor that work in very different ways.
Bipolar and MOS

## Slide 4: Electronic Circuits and Systems EEE211
Within each of these families there are two types of transistor:
Bipolar transistors can be made either as npn or pnp types.
Bipolar npn
C
E
B
Bipolar pnp
E
C
B
MOS transistors can be made either as n-channel or p-channel types. MOS transistors can be further classified as ‘enhancement’ devices (normally off) or ‘depletion’ devices (normally on)
NMOS n-channel depletion
D
S
G
NMOS n-channel enhancement
D
S
G
PMOS p-channel depletion
S
D
G
PMOS p-channel enhancement
S
D
G
The arrow is placed on the emitter (BJT) or source (MOST) and indicates direction of conventional current flow through the device

## Slide 5: NPN PNP transistor circuit
Vg
1mV
Rg
750
2.2u
C1
Q1
Re1
3.9k
C3
82u
i
in
Q2N2222
Rc1
Q2
Q2N2907A
Re2
2k
Ce2
6.8u
Vcc
Q2N2222
Q3
Rc2
6.2k
Rc3
3.48k
i
out
Vee
Re3
6.2k
C2
1u
v
out
RL
1k
Rf 26.1k
Feedback
12V
12V
Vcc
Vcc
Vee
Vee
+
+
-
-
4.7k
ic3

## Slide 6: Electronic Circuits and Systems EEE211
The bipolar junction transistor (BJT)
Diodes and bipolar transistors are made using the same general method but for a bipolar transistor several extra stages are needed to introduce the additional diffusions.
The diagram shows a npn transistor suitable for integrated circuits
Active base – collector junction
Emitter – base junction
N+
P
E
B
C
N-
N+
N+
P-
P+

## Slide 7: Electronic Circuits and Systems EEE211
Injected electrons
Back injected holes
Electron and hole recombination
E
C
B
+
p-type
n-type
+
n-type
IE
IB
IC
Heavily doped emitter and lightly doped base for high emitter efficiency
Very thin base to minimize recombination in transit across the base: 150:1
Low doping in collector for high breakdown voltage
Note: The emitter and collector geometries and doping densities are different, so it is not desirable to use the transistor the other way round – i.e. collector as emitter.
Common-base model

## Slide 8: Electronic Circuits and Systems EEE211
-
+
-
-
-
-
-
-
-
-
-
+
+
+
-
-
-
-
+
+
+
+
+
+
+
-
-
-
-
-
CB
P-type
N-type
+
+
+
+
+
+
CB
+
+
+
+
+
+
+
+
+
-
-
-
-
-
-
-
-
-
IE
N-type
VB
VB
-
+
Note: IE = IC + IB
+
IB
+
IC
IE
VEB
VBC

## Slide 9: Electronic Circuits and Systems EEE211
Common-base model- output characteristics
Active region: b-e is forward biased, c-b is reversed biased
Cut off region: b-e/c-b are both reverse biased
Saturation region: b-e/c-b are forward biased

## Slide 10: Electronic Circuits and Systems EEE211
Typical Output (collector – emitter) characteristics: Common emitter
0
IC
VCE
IB1
IB2
IB3
IB4
IB5
In this region, transistor is ‘saturated’ with charge
Vsat <1.0 v, (but usually  0.2v)
‘Active’ operating region, the transistor characteristics are similar to those of a constant current source controlled by the magnitude of IB. VCE is > 1.0v
Active region: b-e is forward biased, c-b is reversed biased
Cut off : IC = ICEO = ᵝICBO

## Slide 11: Electronic Circuits and Systems EEE211
The BJT in saturation
-
+
-
-
-
-
-
-
-
-
-
+
+
+
-
-
-
-
+
+
+
+
+
+
+
-
-
-
-
-
CB
P-type
N-type
+
+
+
+
+
+
CB
+
+
+
+
+
+
+
+
+
-
-
-
-
-
-
-
-
IE
N-type
VB
VB
IB
IC
IE
VBC
-
-
-
-
-
-
-
+
+
+
+
+
Note
Collector – base junction becomes forward biased – charge floods into collector region from the base
High recombination occurs in collector fed by base current – current gain falls
Large increase in stored charge slows switching time

## Slide 12: Electronic Circuits and Systems EEE211
Typical transistor Input (base – emitter) characteristics
IB
VBE
Vγ ~0.6v
The base – emitter junction is a pn junction and has the expected exponential current – voltage characteristics. The ‘turn – on’ voltage normally allowed is 0.6 volts (silicon transistor) which is a little less than that of a silicon diode (0.7 volts) because the base current is usually much less than in a diode.

## Slide 13: Electronic Circuits and Systems EEE211
IC and IE vs VBE characteristics on Log- Lin scales
Ln (IE, IC )
VBE (linear scale)
Vγ
Working region, n=1 (Ib small, β large)
Resistance volt drop begins to dominate VBE
High level injection n=2
Recombination injection n=2
Current gain β = IC/IB=
Note that the current gain falls at both low and high currents
IB large, β small
IB large β small
IE
IC
In both cases, the ‘-1’ may be ignored when the transistor is operating well above the leakage current IS
where the factor n varies between 1 and 2 and VT = kT/q ≈ 0.025 v at 300 deg K
IC/(IE – IC)

## Slide 14: Electronic Circuits and Systems EEE211
This equation for IC is obeyed over many decades of current
This equation is very important and should be remembered.
Note that this equation suggests that the collector current is independant of the collector – emitter voltage.
However, in practice there is a slight increase of IC with VCE (called the ‘Early Effect’) which arises from base width narrowing as the collector voltage is increased.
(For both IE and IC, the ‘-1’ may be ignored when the transistor is operating well above the leakage current IS)

## Slide 15: Electronic Circuits and Systems EEE211
‘Punch through’
-VA
0
IC
VCE
Punch through
Eventually the base width decreases to zero width and ‘punch through’ occurs. (a form of breakdown)
The collector current rises and the base loses control. The effect can be reversed by reducing the collector voltage provided the transistor is not damaged by excessive heating.
IC
+
+
+
+
+
+
+
-
-
-
-
P-type
N-type
+
+
+
+
+
+
N-type
IB
IE

## Slide 16: Electronic Circuits and Systems EEE211
The ‘ Early effect’
It is found that if the characteristics are extrapolated back to zero current as shown, then they all pass through a common point on the voltage axis at a voltage called the ‘Early voltage’, VA. (named after J.M. Early who first explained the effect)
-VA
0
IC
VCE
IB

## Slide 17: Electronic Circuits and Systems EEE211
The slope on the output characteristic can therefore be taken into account by modifying the equation for IC to give:
VA is typically 30 – 200 volts depending on the type of transistor (npn or pnp, high power or small signal etc)
Exercise:
Consider the circuit opposite where the transistor has negligible Early effect (i.e. flat output characteristic). Assume that the transistor is in the active regime of operation.
What do you expect to happen to the collector current (IC) if:
1) RC is increased (Ans: small reduction due to Early effect)
2) VCC is increased (Ans: small increase due to Early effect)
3) VBE is increased (Ans: large increase up to a maximum of approx VCC/RC at which point the transistor enters the saturation region)
What happens to VCE in each case?
(Ans: 1) reduces, 2) increases, 3) reduces)
VCC
RC
VBE
VCE

## Slide 18: Common Emitter with Time-Varying Input

## Slide 19: Electronic Circuits and Systems EEE211
Common-collector model

## Slide 20: Electronic Circuits and Systems EEE211

## Slide 21: Electronic Circuits and Systems EEE211

## Slide 22: Electronic Circuits and Systems EEE211
Q:
Explain what is meant by the term “small signal equivalent circuit”. How is it used in electronic circuit design?
A:

## Slide 23: Electronic Circuits and Systems EEE211
Suppose we wish to analyse a transistor circuit intended to amplify small a.c. signals (as opposed to simpler logic circuits in which large digital signals are applied to the transistor to make it either ‘ON’ or ‘OFF’).
We will represent the transistor with an equivalent circuit which is substituted in place of the transistor in the real electrical circuit. Unfortunately, the parameters used in the equivalent circuit depend on the DC current flowing through the transistor. The procedure is therefore:
Procedure on Modelling the small a.c. signal behaviour
First analyse the circuit using DC analysis to find the quiescent (DC) conditions applied to the transistor - (do this with any applied ac signal set to zero and replace any capacitances with open circuits (ZC = ∞ for DC)).
Calculate the ac equivalent circuit components that correspond to those DC conditions (some may need to be obtained from the manufacturer datasheet).
Add the external circuit components and solve the resulting a.c. circuit

## Slide 24: Electronic Circuits and Systems EEE211
A.C. Transistor Models
where all the parameters depend (to varying extent) on the D.C. bias level, ICQ and VCQ
Note that this a basic model that is suitable for low frequencies only.
Later we we will seek a more accurate model suitable for high frequencies..
In this module we will choose the ‘hybrid ’ model which is available in two (equivalent) forms:
r
βib
ro
b
e
c
ib
e
ic
Which equivalent circuit should we choose? There are several, and which is best depends on the circuit being analysed. However, they should all give the same answer. (hybrid-π, T etc)
r
gmv
ro
b
e
c
v
e
ic

## Slide 25: Electronic Circuits and Systems EEE211
Modelling the input side
The input to the transistor is modelled as a simple resistor with a value equal to the inverse of the slope of the input characteristics, measured at a point set by the DC bias on the transistor. Small changes in VBE (= vbe) cause corresponding small changes in IB (= ib) that are related by:
ro is 1/slope of the output characteristics at the appropriate value of ICQ
ΔVBE
IB
VBE
ΔIB
IBQ
rπ = ΔVBE / ΔIB
rπ is the 1/slope of the input characteristics at the appropriate DC base current IBQ.

## Slide 26: Electronic Circuits and Systems EEE211
Modelling the output side
ro is 1/slope of the output characteristics at the appropriate value of ICQ
-VA
0
IC
VCE
VCEQ
ICQ
IBQ
ro is 1/slope of the output characteristics at the appropriate value of ICQ
The output characteristics can therefore be represented by a constant current generator in parallel with a resistor ro

## Slide 27: Electronic Circuits and Systems EEE211
Note that the controlled current source is modelled using different equations in the two versions of the hybrid π equivalent circuit.
The fact that these are equivalent follows from the definitions of the current gain β and the transconductance, gm.
r
βib
ro
b
e
c
ib
e
ic
r
gmv
ro
b
e
c
v
e
ic
and
  so β = gm r (IMPORTANT – REMEMBER)
then
[ Hint – it’s much easier to remember it this way round - it’s dimensionless !!! ]

## Slide 28: Electronic Circuits and Systems EEE211
Also we have seen that the collector current of a bipolar transistor is given by
where VT = kT/q  0.025 V = 1/40 V @ 300K
hence gm = 40 IC Amps/V (IMPORTANT – REMEMBER)
[ but don’t forget it only applies at 300K !! ]
= transconductance
so

## Slide 29
Part 2: Exercise

## Slide 30
Transistor equivalent circuits
If the transistor parameters are β = 180 and VA = 150V, and it is biased at ICQ = 2mA, determine the values of gm, r and ro.
(80 mA/V, 2.25k, 75k)
Q1 [Q6.1]
(a)
(b)
Repeat part (a) if ICQ = 0.5mA.
(20 mA/V, 9k, 300k)
Q1 & 2
Electronic Circuits and Systems EEE211
With DC bias condition, equivalent Tr characteristics are obtained.

## Slide 31
(a)
(b)
Solution
[Note the approximation VCE = 0 has been made]
Q1 [Q6.1]
Ans Q1
Electronic Circuits and Systems EEE211

## Slide 32
Transistor equivalent circuits
Q2 [Q6.3]
The transistor parameters are β = 125 and VA = 200V. A value of gm = 200mA/V is desired. Determine the collector current required and then find r and ro.
(5 mA, 0.63k, 40k)
Q1 & 2
Electronic Circuits and Systems EEE211
r
gmv
ro
b
e
c
v
e
ic
r
βib
ro
b
e
c
ib
e
ic
Equivalent Circuits

## Slide 33
Q2 [Q6.3]
The transistor parameters are β = 125 and VA = 200V. A value of gm = 200mA/V is desired. Determine the collector current required and then find r and ro.
Solution
.
Ans Q2
Electronic Circuits and Systems EEE211

## Slide 34: Electronic Circuits and Systems EEE211
A design example
Determine suitable values for the unspecified resistors in the common emitter circuit shown below, to give a voltage gain v0/vi = 200. Assume the transistor output resistance is infinite (i.e. neglect the Early effect)
ZTX450
RC
10 v
0 v
vin
Vout
RB1
RB2
RE
CE

## Slide 35: Electronic Circuits and Systems EEE211
Assume that the values of all capacitors will be chosen so that they will have approximately zero impedance at the frequency of interest.
The ac equivalent circuit is therefore:
r
gmv
ro
b
e
c
v
e
ic
vin
RB2
RB1
RC
vo
ib
Note also that the voltage supply behaves like a very large capacitance to ac signals (and therefore has zero impedance)
To calculate the required values for IC and RC

## Slide 36: Electronic Circuits and Systems EEE211
Noting that in this example
Then the voltage gain =
or
So we choose Ic = 10mA and RC = 500Ω to give the required voltage gain.
Note that IcRc is the DC voltage drop across RC.
The maximum possible value for this is set by the magnitude of the supply voltage. Thus there is a limit to how much gain can be achieved with a simple single stage amplifier with a resistive load.

## Slide 37: Electronic Circuits and Systems EEE211
Extract from ZTX450 data sheet
ZTX450 - Silicon planar medium power transistor
Part number | VCEO V | IC A | ICM A | PD W | hFE |  |  | VCE(sat) |  |  | fT MHz | RCE(sat) mΩ | Price ($) 1k† | Package
 |  |  |  |  | Min | Max | @ IC A | Max mV | @ IC A | @ IB mA |  |  |  | 
ZTX450 | 45 | 1 | 2 | 1 | 100 15 | 300 - | 0.15 1 | 250 | 0.15 | 15 | 150 | - | 0.200 | E-Line
We take 100 ≤ β ≤ 300 to be appropriate at this current level
To calculate a suitable value for RE.
Note that the transistor current gain is a very poorly controlled parameter. It can vary considerably between different transistors even of the same type. Special measures need to be taken to ensure that this variation does not prevent the amplifier from working correctly, for any transistor of the specified type. This is the purpose of RE in the circuit.

## Slide 38: Electronic Circuits and Systems EEE211
So in order to meet the gain requirement, the quiescent collector current ICQ must not be less than 10mA even for the ‘worst case’ transistor. The worst case transistor will have β = 100 in this example.
We also want to prevent the collector current becoming too large when a transistor at the high gain limit (β = 300) is used because this will limit the maximum undistorted output voltage (see question later).
Ideally, the bias point should be located near centre of load line to allow maximum swing without distortion (but more on this later)
ICQ
‘Load line’
0
IC
VCE
A higher gain transistor will cause the bias point to move up the load line, away from the ideal mid point position

## Slide 39: Electronic Circuits and Systems EEE211
The usual practice to allow 5% ~ 10% of the supply voltage to be dropped across RE ( i.e. 0.5 ~ 1v in our case) for the negative feedback to be effective.
Suppose we choose 10%, so for 1v drop and ICQ= 10mA, RE = 1/(10x10-3) = 100 Ω
Any variation in ICQ is controlled by the emitter resistor RE. If ICQ (~ IEQ) increases then the voltage across RE also increases and the DC bias across the emitter – base of the transistor is reduced. This acts to oppose the initial increase in ICQ.
It is an example of negative feedback that stabilises the DC bias of the transistor.
ZTX450
500
10 v
0 v
RB1
RB2
RE
To calculate a suitable value for RE.

## Slide 40: Electronic Circuits and Systems EEE211
To calculate suitable values for RB1 and RB2 we replace the bias resistor circuit by it’s Thevenin equivalent circuit and all capacitors by open circuits (because it is a D.C. analysis)
ZTX450
500
10 v
0 v
RB1
RB2
RE
ZTX450
500
10 v
0 v
RTH
VTH
RE
10mA (β = 100)
→
To calculate suitable values for RB1 and RB2.

## Slide 41: Electronic Circuits and Systems EEE211
We now use the second design guideline introduced last year:
This guideline, together with the value already chosen for RE , is intended to give an acceptable limit to the range of ICQ values that could result from 100 < β < 300
RTH  0.1(β+1)RE
Using this guideline with a ‘worst case’ β = 100 gives:
ZTX450
500
10 v
0 v
RTH
VTH
RE
IC
0. 6v
IB
+
-
IE = IC+IB
=100

## Slide 42: Electronic Circuits and Systems EEE211
Kirchoff’s Voltage Law applied to the base circuit gives:
So for β =100, VBE = 0.6v and ICQ = 10mA then VTH = 1.71 v
Noting that:
ZTX450
500
10 v
0 v
1010
VTH
100
IBQ
β IBQ

## Slide 43: Electronic Circuits and Systems EEE211
Finally we replace VTH and RTH by two base bias resistors :
Giving: RB1 = 5.9k , RB2 = 1.22k
ZTX450
500
10 v
0 v
RTH
VTH
IC
0. 6v
IB
+
-
IE = IC+IB
100
ZTX450
500
10 v
0 v
RB2
100
RB1
→

## Slide 44: Electronic Circuits and Systems EEE211
Adding the external circuit components to the ac equivalent circuit for the transistor gives:
Neglecting the Early effect means r0 → ∞
r
gmv
ro
b
e
c
v
e
ic
vin
RB2
RB1
500
vo
ib
Since vin = vπ then voltage gain Av = vo/vin = -500 x gm = -500 x 0.4 = -200 (as expected).
Now that the D.C. analysis is complete and we know ICQ, RB1 and RB2, we can now complete the a.c. analysis to calculate the input and output impedances.
Input impedance = RB1//RB2//r = RTH//rπ = 1010//250 = 200 (assuming β=100)
Output impedance = 500//r0  500 
gm = 40IC = 40 x 10 x 10-3 = 0.4 amps/volt

## Slide 45: Electronic Circuits and Systems EEE211
ZTX450
500
10 v
0 v
5.9k
1.22k
100
Note:
For DC bias conditions the load line has a slope of 1/(RC+RE) but for ac signals, RE is shorted by the capacitor CE and the operating point moves along a load line with slope 1/RC instead. Both lines pass through the chosen DC operating point. This affects the maximum voltage swing that can be achieved without distortion.
The bias point in this example is not quite optimally placed on the load line. This is a consequence of the voltage gain requirement.
VCE
10
4
16.7
0
IC (mA)
10
9
DC load line slope 1/600
AC load line, slope 1/500
0
0.2

## Slide 46: Lectures 3 A Review on Transistor
Single Base Resistor Biasing

## Slide 47: Lectures 3 A Review on Transistor
Common Emitter with Voltage Divider Biasing and Emitter Resistor

## Slide 48: Question:

## Slide 49: Question:
Solution:

## Slide 50: Question:

## Slide 51: Lectures 3 A Review on Transistor
Positive and Negative Voltage Biasing

## Slide 52: Question:

## Slide 53: Question:
Solution:

## Slide 55: Electronic Circuits and Systems EEE211
ZTX450
500
10 v
0 v
5.9k
1.22k
100
For the design example in lecture
Allow 0.2 volts for the saturation voltage VCE(SAT)
What is the maximum output signal amplitude possible from this design without distortion when a) β=100 and b) β=300 ? (3.8v, 3.38v)
What is the total current drawn by the circuit when β = 100? (11.4mA)
3. If the circuit was required to give a voltage gain of 300 when β = 100, calculate the new value required for RE and the corresponding maximum possible output signal amplitude without distortion? (66.7 ohms, 1.3v)

## Slide 56: Electronic Circuits and Systems EEE211
(a) For β = 100, ICQ = 10 mA
VCEQ = 10 – [(500+100) x 10 x 10-3] = 4 v
Maximum voltage swing without distortion
= 4 – 0.2 = 3.8 v
Answer Q1
Voltage gain = 40 x 10.7 x 10-3 x 500 = 214
VCE
10
4
16.7
0
IC (mA)
10
9
DC load line
AC load line
0.2
VCE
10.7
3.58
16.7
0
IC (mA)
10
9
DC load line
AC load line
0.2
(b) For β = 300, ICQ = 10.7 mA ,
VCEQ = 10 – [(500+100) x 10.7 x 10-3] = 3.58 v
Maximum voltage swing without distortion
= 3.58 – 0.2 = 3.38 v
Voltage gain = 40 x 10 x 10-3 x 500 = 200
Total current drawn when β = 100 is: ICC = 10mA + 10/(5.9k + 1.22k) = 11.4 mA
Answer Q2

## Slide 57: Electronic Circuits and Systems EEE211
(a) For β = 100, ICQ = 15 mA
VCEQ = 10 – [(500+66.7) x 15 x 10-3] = 1.5 v
Maximum voltage swing without distortion
= 1.5 – 0.2 = 1.3 v
Answer Q3
VCE
15
1.5
17.6
0
IC (mA)
10
9
DC load line
AC load line
0.2
Voltage gain = 40 x 15 x 10-3 x 500 = 300
Required voltage gain =
The usual practice to allow 5% ~ 10% of the supply voltage to be dropped across RE ( i.e. 0.5 ~ 1v in our case) for the negative feedback to be effective.

## Slide 58: Electronic Circuits and Systems EEE211
In this lecture we have:
Seen how the bipolar transistor works in the active region and how saturation, the Early effect and punch through occurs.
Seen how the basic hybrid- equivalent circuit is able to model the characteristics of a BJT at low frequencies
Reviewed the procedure required to design a common emitter amplifier that is tolerant of manufacturing variations in the transistor characteristics
Identified the distinction between D.C. and A.C. load lines and seen how to determine the maximum output voltage swing without distortion.
Seen how the gain of the basic common emitter amplifier circuit is limited by the supply voltage and the required output voltage swing.
Seen how to calculate the key parameters of the basic equivalent circuit from gm = 40 ICQ , gmr = β and ro = (VA + VCEQ)/ICQ

## Slide 59: Electronic Circuits and Systems EEE211
1) Chapter 6 in textbook for more information
2) In next lecture we will study the basic BJT amplifier circuits configuration