## Slide 1: Electronic Circuits and Systems EEE211
Introduction to the basic bipolar transistor amplifier configurations
Dept. of Electrical & Electronic Engineering
XJTLU

## Slide 2
Golden Rules for drawing equivalent circuits
Draw the equivalent circuit of the transistor first
Replace capacitors with zero impedances (we are interested in ‘mid-frequency’ regimes where the impedance of the circuit capacitors will normally be zero)
3. Identify the a.c. grounds (remember that voltage supplies behave like a zero resistance for a.c. signals !)
4. Add the remaining circuit components to obtain the complete equivalent circuit.
We first extend the transistor equivalent circuit to include the internal base resistance, rb
Electronic Circuits and Systems EEE211

## Slide 3
What is the internal base resistance rb ?
e
N+
P
b
N-
N+
N+
P-
P+
c
rb
region b’
rb
r
gmv
ro
b
e
v
b’
vbe
c
e
So the equivalent circuit now becomes:
rb is typically a few tens of ohms and becomes particularly important at high frequencies.
rb represents the resistance of semiconductor material between the external base contact b and the active internal base region b’
Electronic Circuits and Systems EEE211

## Slide 4
Having established our model for the bipolar transistor, we are now in a position to analyse the four basic amplifier configurations.
We will see that each configuration has particular properties that we can usefully employ when building up more complex electronic circuits.
2) Common emitter with emitter degradation (CE-ED)
3) Common collector (CC) - also known as emitter follower (EF)
4) Common base (CB)
1) Common emitter (CE)
Basic bipolar transistor amplifier configurations
Electronic Circuits and Systems EEE211

## Slide 5
Part 1: Common Emitter (CE) and
Common Emitter with Emitter Degradation (CE-ED)
Electronic Circuits and Systems EEE211

## Slide 6
The common emitter amplifier (CE)
We have already analysed an example of this circuit, but note the addition of several extra components here.
vS
i
i
R
1
i
c
R
c
R
2
R
E
C
E
R
L
vo
0V
+V
cc
C
c
C
c
RS
The full equivalent circuit would be:
v
r
E
B
i
i
g
m
v

C
i
c
R1
R2
r0
RC
RL
rb
vo
vS
RS
CC
CC
CE
RE
Electronic Circuits and Systems EEE211

## Slide 7
We now make three important simplifying assumptions:
The frequency of the input signal will be assumed to be low enough to be able to ignore the transistors internal capacitances. (The effect of these will be explained later)
Both coupling capacitors Cc are assumed to be large enough to have zero impedance (i.e. short circuits) at the signal frequency of interest
The emitter capacitance will be assumed to be large enough to have zero impedance at the frequency of interest
Electronic Circuits and Systems EEE211

## Slide 8
With the assumptions listed, the full equivalent circuit (above) simplifies considerably to give:
v
r
E
B
i
i
g
m
v

C
i
c
R1
R2
r0
RC
RL
rb
vo
vS
RS
CC
CC
CE
RE
v
S
v
r
E
B
i
i
g
m
v

C
v
o
R
Rt
rb
vbe
RS
B’
ro//RC//RL
R1//R2
Electronic Circuits and Systems EEE211

## Slide 9
v
S
v
r
E
B
i
i
g
m
v

C
v
o
R
Rt
rb
vbe
RS
B’
( chain rule )
Note the reduction in voltage gain caused by:
1. the finite value of rb
2. the series resistance of the source RS
3. the finite value of ro (which reduces Rt)
If rb is negligible compared to rπ, (it often is) then vbe = v and the voltage gain becomes:
( so to maximise the voltage gain make R large compared to r so that the signal current flows into the transistor base rather than to ground through R !)
CE Voltage gain
Remember the voltage divider rule !
Electronic Circuits and Systems EEE211

## Slide 10
The product ICRC is the DC voltage drop across the collector load resistor RC
so to achieve the highest possible gain requires this to be a maximum. But the supply voltage is shared across RC, RE and the transistor.
If R >> r , rπ >> RS and ro >> RC//RL , then
The maximum voltage gain is achieved if RL >> RC giving:
Design problem !!
assuming IE ~ IC
The voltage across RE is required to be ~0.1 VCC for a good design, so increasing the voltage across RC can only be achieved (for a given value of VCC) at the expense of reducing VCE. The absolute maximum voltage gain will occur when VCE → 0, giving in the limit:
Electronic Circuits and Systems EEE211

## Slide 11
The gain can only be further increased by increasing both the supply voltage and ICQ – not something that is desirable, especially if low power consumption from the supply is required.
maximising the voltage gain requires the transistor to be biased towards the top end of the DC load line
VCE
ICQ
VCEQ
VCC
DC load line (slope = 1/(RE+RC)
0
ICQ(RC+RE)
Supply voltage
0
This problem can be solved using an ‘active load’ – but it needs a major circuit re-think to work properly. We will return to this problem later
Very little movement of the bias point is possible without causing the output waveform to be distorted
IC
AC load line (slope = 1/RC)
Electronic Circuits and Systems EEE211

## Slide 12
This means that :
the voltage gain that can be achieved using a simple CE amplifier with a resistance load is limited to:
2. the maximum undistorted output voltage amplitude at this bias point is very small.
3. Higher gains imply higher power consumption from the supply.
Electronic Circuits and Systems EEE211

## Slide 13
VCE
ICQ
VCEQ
VCC
0
ICQ(RC+RE)
0
IC
Electronic Circuits and Systems EEE211

## Slide 14
CE Current gain
If RC >> RL also, then the current gain is maximised and Ai  β
Remember how current divides between two resistors in parallel !
r
E
B
ii
g
m
v

C
v
o
R
ro
rb
B’
vS
RS
RC
io
v
RL
E
If rπ>>rb , R >> r and ro >> RC then
Electronic Circuits and Systems EEE211

## Slide 15
CE Input resistance (at low frequency)
r
E
B
ii
g
m
v

C
v
o
R
RC
rb
B’
vS
RS
1. Input resistance – ‘looking into’ the base of the transistor itself is:
1
vbe
vi
ib
CE Output resistance (at low frequency)
Output resistance – as ‘seen’ by the load RL = RC//ro
2. Input resistance - as ‘seen’ by the ac signal source is:
2
RL
r0
Electronic Circuits and Systems EEE211

## Slide 16
Common emitter with emitter degradation (CE-ED)
For simplicity, we initially assume r >> rb, R = R1//R2   and ro  
v
i
R
i
R
C
R
o
io
R
L
v
o
R
E
R1
R2
ii
rb
r
E
B
ii
β
ib
C
vo
R
ro
B’
RC
io
RE
RL
vi
ib
CE-ED input resistance
ib
ic
N.B. R has to be at least ~10 times ri to be considered negligible.
if β >>1
Ri = R // (r + rb + (1+β)RE)
If R and rb are not neglected then
Electronic Circuits and Systems EEE211

## Slide 17
Note that gmRE=40ICRE, so the volt drop across RE only has to be >> 1/40 volt for this approximation to be valid !
CE-ED voltage gain
But gm = β/r
if R//Ri >> RS and β >>1
rb
r
E
B
ii
β
ib
C
vo
ro
B’
RC
io
RE
RL
vi
ib
ib
ic
v
S
RS
R
Electronic Circuits and Systems EEE211

## Slide 18
CE-ED current gain (assuming ro →∞ and R >> ri)
CE-ED Output resistance (assuming ro →∞)
rb
r
E
B
ii
β
ib
C
vo
R
ro
B’
RC
iO
RE
RL
vi
ib
iC
and
Output resistance =
(same as CE)
Electronic Circuits and Systems EEE211

## Slide 19
[ Note on CE-ED Output resistance
Assume RS << rπ. Then inject a small current io into the collector terminal. This will cause a small increase in vo
But vπ= - io (rπ//RE)
So the effective resistance from collector to emitter is even larger than ro
rb
r
E
B
gm
vπ
C
vo
ro
B’
RC
io
RE
RL
ib
v
S
RS
R
vπ
i1
if gmro>>1,
The output resistance seen by the load is the resistance from collector to emitter in parallel with RC so normally the approximation Ro ≈ RC is justified ]
Electronic Circuits and Systems EEE211

## Slide 20
Part 2: Exercise (CE & CE-ED)

## Slide 21
Q3 [Q6.7]
For the circuit shown, β = 120, VCC = 5V, VA = 100V and RB = 25k.
(a) Determine VBB and RC such that r = 5.4k and the Q-point is in the centre of the load line. (0.82 V, 4.55k)
(b) Find the resulting small-signal voltage gain Av = vo/vs (-17.4)
Vcc = 5v
0 v
vo
VCE
RC
RB
VBB
+
-
vS
VBE
iC
IB
VRC
β = 120
Q3
Electronic Circuits and Systems EEE211

## Slide 22
For the Q-point to be in the centre of the load line, VCE = VRC = 2.5v=0.5Vcc
For the base circuit
(a) DC condition
Solution
Q3 [Q6.7]
Ans Q3 a
Electronic Circuits and Systems EEE211
Must remember these relations
Since VBE(on)=0.7

## Slide 23
(b) AC condition
r
gmvπ
ro
B
E
C
v
E
ic
vS
+
-
RC = 4.55k
vo
ib
VS
RB=25k
Ans Q3 b
Electronic Circuits and Systems EEE211



## Slide 24
Q4
The parameters of the transistor in the figure are β = 150 and VA = (No Early effect).
Determine R1 and R2 to obtain a bias stable circuit with the Q-point in the centre of the load line. (20.1k, 3.5k)
Q4 [Q6.11]
[Hint: to provide adequate bias stabilization, make RTH one tenth of (1+β)RE where RTH is the Thevenin equivalent source resistance of the base circuit. ]
(b) Determine the small-signal voltage gain Av = vo / vi. (-5.76)
RC = 1.2k
5 v
0 v
vi
+
-
vo
R1
R2
-5 v
RE = 0.2k
β = 150
0 v
Electronic Circuits and Systems EEE211

## Slide 25
Solution
[Neglecting IB compared to IC so that IE  IC]
(a)
To bias in the centre of the load line,
Ans Q4a
For stability, make
Electronic Circuits and Systems EEE211

## Slide 26
But RTH is the DC Thevenin resistance of the base circuit
eqn (1)
R1 = 20.1 k, R2 = 3.5 k
Solution of equations (1) and (2) gives
(ignoring effect of IB)
eqn (2)
and
Ans Q4a
For the base circuit,
Electronic Circuits and Systems EEE211
(in Lecture 2)
(in Lecture 2)

## Slide 27: Electronic Circuits and Systems EEE211
r
βib
ro
B
E
C
v
E
ic
vi
+
-
R2
R1
1.2k
vo
ib
RE
VRE
Ans Q4b
Common Emitter with Emitter Degradation Amplifier(CE-ED)
Check Lecture 3 pp. 15

## Slide 28: Electronic Circuits and Systems EEE211
Q5 [Q6.14]
For the circuit shown below, the transistor parameters are β = 100 and VA = .
Design the circuit such that ICQ = 0.25mA and VCEQ = 3V. (RE = 16.6k, RC = 11.3 k)
Find the small signal voltage gain Av = Vo/Vi. ( -56.2 )
Find the input resistance seen by the signal source Vi. (14.34k )
RC
5 v
0 v
Vi
+
-
vo
RB = 50k
-5 v
RS = 100
CE
RE
Q5

## Slide 29: Electronic Circuits and Systems EEE211
Ans Q5
Solution
For the base-emitter DC circuit,
For VCE = 3V, required volt drop across RC is given by:
Hence
DC condition
For IC = 0.25mA,
Capacitor open

## Slide 30: Electronic Circuits and Systems EEE211
Ans Q5
AC condition
Input impedance seen by signal source = ri // RB = 14.34 k
r
βib
ro
B
E
C
v
E
ic
vi
+
-
RB= 50k
11.3k
vo
ib
RS=100
Same as Q4

## Slide 31: Electronic Circuits and Systems EEE211
Q6 [Q6.25]
For the transistor in the circuit shown below, the parameters are β = 100 and VA = .
(a) Determine the Q-point. (IC = 1.69 mA, VCE = 5.44 V)
(b) Find the small circuit parameters gm, r and ro. (68.mA/V, 1.47k, ∞)
(c) Find the small signal voltage gain AS = vo/vS. and the small signal current gain AiS = io/iiS. (-1.065, -1.59 )
(d) Find the input resistance Rib and RiS. (304.5k, 10.2k )
(e) Repeat part (c) if RS = 0. (-1.12, -1.59 )
RC = 6.8 k
16 v
-6 v
vS
+
-
vo
RB = 10 k
RE = 3 k
RS = 0.5 k
RL = 6.8 k
Ans Q6

## Slide 32: Electronic Circuits and Systems EEE211
Q6a
Solution
DC condition
For the base-emitter DC circuit,

## Slide 33: Electronic Circuits and Systems EEE211
Q6b
(b) All parameter was derived in Lecture 2 pp. 19-21
because VA = 


## Slide 34: Electronic Circuits and Systems EEE211
Q6c&d
(c) & (d)
r
βib
ro
B
E
C
v
E
ic
vS
+
-
RB= 10k
RC=6.8k
vo
ib
RE=3 k
VRE
RL = 6.8k
io
RS= 0.5k
rib
riS
vb
iS

## Slide 35: Electronic Circuits and Systems EEE211
Q6c&d
r
βib
ro
B
E
C
v
E
ic
vS
+
-
RB= 10k
RC=6.8k
vo
ib
RE=3 k
VRE
RL = 6.8k
io
RS= 0.5k
rib
riS
vi
iS
(e) For RS = 0
AiS is unchanged

## Slide 36
Part 3: Common Collector (CC)

## Slide 37
rb
ib
r
E
B
ii
βib
C
vo
R
ro
B’
RE//RL
vi
vS
RS
vπ
CC Input resistance
R
L
vo
0V
+V
cc
v
i
ii
R
1
R
2
i
o
vS
RS
Common collector (CC) (or Emitter follower)
In practice rb << rπ and can usually be ignored, but R often cannot.
If R and rb are not neglected then
R
E
Electronic Circuits and Systems EEE211
which is similar to Ri in CE-ED configuration

## Slide 38
CC Voltage gain
So for the common collector amplifier, the voltage gain is less than 1 and is non-inverting
rb
ib
r
E
B
ii
βib
C
vo
R
ro
B’
RE//RL
vi
vS
RS
vπ
To calculate
where
Ri
( for β >>1 and noting that β = gmrπ )
Electronic Circuits and Systems EEE211

## Slide 39
Note : More generally, the total output resistance is the Thevenin resistance of the base circuit divided by β, plus 1/gm, all in parallel with RE - It is usually a very low value
CC Output resistance
The output resistance Ro is RE in parallel with the impedance ‘looking into’ the emitter of the transistor.
To determine the impedance ‘looking into’ the emitter of the transistor, first imagine removing RE and then draw a small amount of current Δio from the emitter of the transistor as shown in the figure. The output voltage vo will fall by a small amount Δvo . The output resistance ‘looking into the emitter’ is then given by ro = |Δvo / Δio| .
Because of the small fall in output voltage, Δvo , the base current ib will increase by Δvo/(RS + r) and the collector current will increase by β Δvo/(RS + r). Thus the total change of current from the emitter because of Δvo is Δio = (β+1) Δvo/(RS + r).
The output resistance ‘looking into the emitter’ of the transistor is therefore:
where re =1/gm
rb
ib
r
E
B
ii
βib
C
-Δvo
R
ro
B’
vi
vS
RS
vπ
RE
Δio
Ro
Now re-attach RE. The total output resistance is then
Electronic Circuits and Systems EEE211

## Slide 40
CC Current gain
Neglecting rb and ro
rb
ib
r
E
B
ii
βib
C
vo
R
ro
B’
RE
vi
vS
RS
vπ
io
ie
RL
If R >> rπ +(1+β)RE//RL
Take care - R is not often >> rπ +(1+β)RE//RL !
Electronic Circuits and Systems EEE211

## Slide 41
This circuit is therefore very useful as a ‘buffer’ .
It is often used to isolate two circuits from each other so circuit 2 does not draw current from circuit 1
Circuit 1
Circuit 2
CC ‘buffer’
The high input impedance means it draws very little current from circuit 1 and is also able to drive circuit 2 easily from its low output impedance and high current gain.
A voltage gain of very nearly unity means that the signal from circuit 1 is passed onto circuit 2 unchanged
So the common collector circuit has a very high input impedance, low output impedance and voltage gain ~ 1
Electronic Circuits and Systems EEE211

## Slide 42: Electronic Circuits and Systems EEE211
We can understand a constant voltage source fairly easily because we use them almost every day of our lives.
The source keeps its output terminal voltage constant regardless of the current drawn from it. But it does not necessarily stay constant with time. Examples of sources that try to meet the definition of a constant voltage source would be a car battery and the ac mains.
Pause for thought !!
We will now begin to describe the behaviour of the system with reference to ‘constant voltage’ and ‘constant current’ sources.
But what exactly is a ‘constant voltage’ source and ‘constant current’ source?
Current I
Voltage V
VS
A constant voltage source keeps the voltage constant at VS regardless of the current drawn from it. It’s output resistance is zero
A practical voltage source will not quite achieve the ideal behaviour. It will have an upper current limit and its output resistance will be a small but finite value
Rint = - slope = RO
Rint = - slope = 0

## Slide 43
Part 4: Exercise (CC)

## Slide 44: Electronic Circuits and Systems EEE211
Q7 [Q6.39]
The transistor parameters for the circuit shown are β = 180 and VA = .
Find ICQ and VEQ. (15.7mA, 10.15 V)
Plot the DC and AC load lines.
Calculate the small signal voltage gain. (0.81)
(d) Determine the input and output resistances, rib and ro ( 34.2k, 6.2k)
+
-
R2 = 10k
CC2
R1 = 10k
RS = 1k
CC1
rib
RE = 500
rO
β = 180
vo
RL = 300
9 v
-9 v
vi
Q7

## Slide 45: Electronic Circuits and Systems EEE211
Solution
(a) DC conditions
9 v
-9 v
RE = 500
RB = 5k
VB = 0 V
Q7a

## Slide 46: Electronic Circuits and Systems EEE211
(b)
IC
VCE
18 V
36 mA
ICQ = 15.7 mA
VCEQ = 10.15 V
Slope = -1/(RE//RL) = -1/187
Slope = - 1/RE = -1/500
Q7b

## Slide 47: Electronic Circuits and Systems EEE211
r
βib
ro
B
E
C
v
E
ic
vS
+
-
R2= 10k
ib
RE=500
VO
RS= 1k
rib
riS
vi
iS
RL=300
R1= 10k
(c) AC conditions
Q7c&d
In an exam – USE THE AMPLIFIER PROPERTIES SHEET !!

## Slide 48: Electronic Circuits and Systems EEE211
since re << RE
Q7d
where
+
-
R2 = 10k
CC2
R1 = 10k
RS = 1k
CC1
rib
RE = 500
rO
β = 180
vo
RL = 300
9 v
-9 v
vi
Remember ro

## Slide 49: Electronic Circuits and Systems EEE211
Q8 [Q6.43]
Consider the emitter-follower amplifier shown below. The transistor parameters are β = 100 and VA = 100 V.
(a) Find the output resistance rO. (111Ω)
(b) Determine the small signal voltage gain for (i) RL = 500  and (ii) RL = 5k.
( i) 0.817, ii) 0.976 )
3 v
-3 v
VS
+
-
RS = 10k
RL
vO
β = 100
IQ = 2mA
CC
rO
Q8

## Slide 50: Electronic Circuits and Systems EEE211
3 v
-3 v
VS
+
-
RS = 10k
β = 100
IQ = 2mA
(a)
DC conditions
Q8a
Almost same !
c.f. 2 mA
c.f. 20 µA
c.f. 80 mA/V
c.f. 1250 Ω
c.f. 111 Ω

## Slide 51: Electronic Circuits and Systems EEE211
r
βib
ro
B
E
C
v
E
ic
vS
+
-
ib
VO
RS= 10k
rib
vi
iS
RL
(b)
(i) Voltage gain if RL = 500 :
Therefore need rib.
Note the answer given in the textbook does not take into account RS - gives Avi rather than Avs
ro = VA/ ICQ=100/1.98
= 50.5 kΩ

## Slide 52: Electronic Circuits and Systems EEE211
(ii) Voltage gain if RL = 5k :
( Again, the textbook gives Avi rather than Avs )
Q8b(ii)

## Slide 53
Part 5: Common Base (CB)

## Slide 54
Common Base (CB)
Typical circuit in practice
0V
+VCC
Rs
vs
vi
ii
RC
RE
io
R2
vo
R1
Replacing the capacitors with zero impedances, the ac equivalent circuit (outside the transistor) may be re-drawn as:
RL
0V
Rs
vs
vi
RC
RE
io
vo
RL
Ri
Ro
Electronic Circuits and Systems EEE211

## Slide 55
CB current gain
Now also replacing the transistor with its equivalent circuit (neglecting rb and ro) gives:
if β >> 1
gmv = βib
0V
Rs
vs
vi
RC
RE
io
vo
RL
ii
rπ
ic
ib
vπ
C
E
B
if RE >> re (= 1/gm)
Note Ai <1
Electronic Circuits and Systems EEE211

## Slide 56
CB input resistance
gmv = βib
0V
Rs
vs
vi
RC
RE
io
vo
RL
ii
rπ
ic
ib
vπ
re
C
E
B
Ri
Imagine drawing out a small current Δie from the emitter of the transistor at point E. The potential at E will fall slightly by Δvπ and the input resistance will be given by |Δvπ/Δie|
Electronic Circuits and Systems EEE211

## Slide 57
CB voltage gain (neglecting ro)
gmv = βib
0V
Rs
vs
vi
RC
RE
io
vo
RL
ii
rπ
ic
ib
vπ
re
C
E
B
NB - this amplifier does not invert the signal (Av is positive). A positive going change in vs reduces the bias on the emitter, reducing the collector current and therefore increasing the collector voltage
Note vi = - vπ so vo = -gmvπ RC//RL= gmviRC//RL . Therefore vo/vi =gmRC//RL
Electronic Circuits and Systems EEE211

## Slide 58
CB output resistance
gmv = βib
0V
Rs
vs
vi
RC
RE
io
vo
RL
ii
rπ
ic
ib
vπ
re
C
E
B
(Neglecting ro – see previous comment on CE-ED output resistance)
Electronic Circuits and Systems EEE211

## Slide 59
Part 6: Exercise (CB)

## Slide 60: Electronic Circuits and Systems EEE211
Q9 [Q6.56]
For the circuit shown below, the transistor parameters are β = 100 and VA = .
Determine the DC voltages at the collector, base and emitter terminals.
(1.7 V, 1.2 V, 0.5 V)
(b) Determine the small signal voltage gain Av = vo/vS (18.87 )
(c) Find the input resistance Ri. ( 47.6 Ω )
5 V
0 V
vS
+
-
RE = 1k
RS = 50
CC1
RB=100k
β = 100
vO
RL = 1 k
Ri
CC2
ICC = 0.5 mA
Q9
Common Base circuit

## Slide 61: Electronic Circuits and Systems EEE211
Q9a
(a) Consider DC conditions
5 V
0 V
RE = 1k
ICC = 0.5 mA
β = 100
RB = 100k
Because we don’t know VCEQ

## Slide 62: Electronic Circuits and Systems EEE211
(b) Consider AC conditions
r
gmv
ro
B
E
C
v
E
ic
vS
+
-
RB=100k
vO
ib
RL = 1k
RS= 50
RE= 1k
(c)
Q9b

## Slide 63: BJT Amplifier with Active Load
What does a current source look like ?

## Slide 64: Characteristics of Bipolar Circuit with Active Load

## Slide 65
Summary of properties of amplifier configurations
Property | AV | AI | Rin | Rout | Usage
CE | High | High | Medium | High | Most useful, general purpose
CE+ED | Low | High | High | High | RE constitutes feedback – sacrifice AV to increase Rin – also gives increased stability: (less dependent on o and temperature).
CC | Low (< 1) | High | High | Low | Impedance matching – presents high input resistance to source to low output resistance to the load. (Also very linear –- used in power amp. output stages - gives current gain ). Good high frequency performance.
CB | High | Low (<1) | Low | High | Impedance matching – presents low input resistance to source and high output resistance to load. Good high frequency performance.(Features in Differential.Amp. – see later)
REMEMBER THESE !
Electronic Circuits and Systems EEE211

## Slide 66
Part 7: Multi-Stage Amplifier Circuits

## Slide 67: Abstraction for an amplifier design
(a) Block diagram view of an amplifier
(b) A high-level circuit model for amplifier
(c) A transistor-level schematic for the amplifier

## Slide 68: Application on Sound System
Specifications: An audio amplifier is to deliver an average power of 0.1 W to an 8 speaker from a microphone produces a 10 mv peak sinusoidal signal and has a source resistance of .

## Slide 69: Example – multi-stage amplifiers
CC –
Emitter follower
Two-stage CE
CC –
Emitter follower
pp. 445, 4th edition

## Slide 70: Example – multi-stage amplifiers
Question:
The parameters for each transistor in the circuit shown in the figure are and .
Determine the small-signal parameter , , and for both transistors.
Determine the small-signal voltage gain , assuming is connected to an open circuit, and determine the gain .
Determine the overall voltage gain . Compare it with the product using the values calculated in part (b)

## Slide 71: Example – multi-stage amplifiers
Solution:

## Slide 72: Example – multi-stage amplifiers
Solution:

## Slide 73: Example – multi-stage amplifiers
Question: The parameters for each transistor in the circuit shown in the figure are and .
Determine the small-signal parameter , , and for both transistors.
Plot the DC and AC load line for both transistors.
Determine the overall voltage gain .
Determine the input resistance and output resistance .

## Slide 74: Example – multi-stage amplifiers

## Slide 75: Example – multi-stage amplifiers

## Slide 76: Example – multi-stage amplifiers

## Slide 77: Example – multi-stage amplifiers

## Slide 78: Example – multi-stage amplifiers

## Slide 79
Electronic Circuits and Systems EEE211
Multi-Stage Circuit Analysis & Design – (Test_Yourself)
1) In the circuit shown in the figure, biasing components have been omitted. The collector currents in transistor Q1, Q2 and Q3 are , and respectively. Assuming and are infinite, and , calculate the transistor trans-conductance () and emitter-base resistance () of each transistor.

## Slide 80
Electronic Circuits and Systems EEE211
2) Calculate the voltage gain of the circuit

## Slide 81
In this lecture we have:
Applied the low frequency transistor equivalent circuit to analyse the four basic transistor ‘building block’ circuits - Common Emitter (CE), Common Emitter with Emitter Degradation (CE-ED), Common Collector (CC) Common Base (CB) transistor amplifiers and obtained expressions for the voltage gain, current gain, input and output resistances.
Noted that the voltage gain that can be obtained from the basic CE amplifier (which has a load resistor) is limited to be less than 40 x supply voltage and requires that the bias position be located at the very top of the load line where the magnitude of the output signal will be very small and the power drawn from the supply relatively large.
Electronic Circuits and Systems EEE211

## Slide 82
Electronic Circuits and Systems EEE211
In next lecture, we will study hybrid-pi model of BJT, for high frequency signal