## Slide 1: Electronic Circuits and Systems EEE211
Differential Amplifier Analysis
Dept. of Electrical & Electronic Engineering
XJTLU

## Slide 2: Electronic Circuits and Systems EEE211
Part 1:
Differential Amplifier and CMRR

## Slide 3
- is an amplifier designed to produce an output voltage vo that represents an amplified version of the difference between two input signals vi1 and vi2.
In an ideal differential amplifier, if the same signal voltage is applied to both inputs at the same time , then vi1 = vi2 and vo should be zero. A signal that appears on both the inputs at the same time in this way is called a ‘common mode’ signal.
The Differential Amplifier
vi1
vi2
vo
Unfortunately, in practice it is found that a small output voltage will be produced in response to a common mode signal. However, a good differential amplifier would have a high gain for the differential signal but a low gain for the common mode signal. This figure of merit is expressed as the ‘Common Mode Rejection Ratio’ of the amplifier (CMMR)
Electronic Circuits and Systems EEE211

## Slide 4
Suppose the input signals to a differential amplifier vi1 and vi2 consist of a common mode voltage vic applied to both inputs and a difference voltage vid shared between them, then
and
vi1
vi2
vo
so
but the common mode signal is equal to the average value of vi1 and vi2
Note that the differential mode signal is simply equal to the difference between the values of vi1 and vi2
Electronic Circuits and Systems EEE211

## Slide 5
What is this ‘common mode’ signal?
In practice, it is often required to amplify very small electrical signals and unwanted interference signals (‘noise’) can be ‘picked up’. Often the noise signal can completely obscure the required signal and an ordinary amplifier would not improve the situation, because it will amplify both the noise and the required signal by the same amount.
For example, if vi1 = 50μV and vi2 = -50μV then vid = 100 μV and vic = 0 μV
Or, if vi1 = 1050μV and vi2 = 950μV, then vid = 100 μV and vic = 1000 μV
This problem can be considerably reduced if a differential amplifier is used and the circuit arranged so that the noise signal is ‘picked up’ in equal amounts (and in phase) on both of its inputs. A good differential amplifier will not amplify the common mode signal (the noise) but will amplify the differential signal (the required signal). In this way the signal/noise ratio is greatly improved
[ This technique will be discussed further in the Instrumentation module ]
Electronic Circuits and Systems EEE211

## Slide 6
transducer
Vs
Interference signal Vn
vn
Vo =AvVs
Av
transducer
Vs
Interference signal Vn
Vs+Vn
Vo =Av(Vs+Vn)
Av
The interference signal can be reduced considerably if a differential amplifier is used and the wires are twisted together so that the area of the pickup loop is minimised. Only a ‘common mode’ signal is now picked up and this should not be amplified by the differential amplifier.
Electronic Circuits and Systems EEE211

## Slide 7
Common mode rejection ratio, CMRR
(3)
Which we want to be as large as possible
Examples of commercial op-amps:
741  = 70 – 90 dB (3,000 to 30,000)
OP07  = 94 – 106 dB (50,000 to 200,000)
This is an important figure of merit for a differential amplifier that tells us how good it is at rejecting the unwanted common mode signal (CM) relative to the differential signal that we want to amplify (DM). We clearly want a high differential gain and a low common mode gain.
As a measure of this, we define
[ Note that for a voltage or voltage gain ratio, dB = 20log10(Ad / Ac) ]
So in these amplifiers, the differential signals are amplified several thousand times more than the common mode signals
Electronic Circuits and Systems EEE211

## Slide 8: Electronic Circuits and Systems EEE211
Part 2:
Long Tailed Pair Circuit and Its DC&AC Analysis

## Slide 9
This basic differential amplifier circuit forms the basis of much more complex differential amplifiers
The ‘long tail’ pair, (or emitter coupled pair)
Note that split supply rails are used so that the input signals can be referenced with respect to ground without adding a DC common mode voltage.
RC
IE1
IE2
vi1
IB1
Q1
Q2
I
o
RE
vi2
IB2
vo
+VCC
P
-VEE
0V
0V
0V
0V
Electronic Circuits and Systems EEE211

## Slide 10
Electronic Circuits and Systems EEE211

## Slide 11
D.C. conditions: explanation of required conditions
Consider the operation of the circuit under d.c. conditions (that is, with the a.c. voltage input signals vi1 = vi2 = 0). The small input signal voltages connected directly to the bases of Q1 and Q2, will hold the base of each transistor close to 0V whilst the emitters of both Q1 and Q2 (point P) will be at ~ -0.6 V due to the forward biased base-emitter diode drop. This voltage will not change significantly under normal conditions, so the combination of RE and VEE constitute a simple current source of magnitude:
Provided that Q1 and Q2 are identical transistors, the current Io will divide equally between them.
The value of RC is chosen with the same considerations as for the common emitter amplifier. The maximum voltage gain can be achieved by arranging a substantial part of VCC to be dropped across it, but the magnitude of the output voltage will be limited.
Electronic Circuits and Systems EEE211

## Slide 12
D.C. analysis
RC
IE1
IE2
Vi1 = 0
IB1
T1
T2
I
o
RE
Vi2 = 0
IB2
+VCC
-VEE
0V
0V
0V
RS1
RS2
IE1
IE2
and
To perform the DC analysis, we first turn down the ac input signals vi1 and vi2 to zero.
Then
Electronic Circuits and Systems EEE211

## Slide 13
If the circuit is balanced so that:
so
and
Eqn 1
Eqn 2
Then eqns 1 and 2 reduce to:
But
so substituting for IB gives
Electronic Circuits and Systems EEE211

## Slide 14
Note that the currents flowing through the two transistors are independent of the values for RC - which will be chosen to ensure the transistors do not saturate at the maximum voltage output swing required. (In fact, the same considerations apply to the choice of RC in this circuit as applied for the common emitter amplifier circuit considered previously)
Note if 2(β+1)RE >> RS (which it almost certainly will be in practice), then
and the current through RE
(as we deduced before)
Although we have simply confirmed the previous result, it does show the condition that needs to be satisfied for it to be valid.
Electronic Circuits and Systems EEE211

## Slide 15
A.C. analysis
Replacing the transistors with their (basic) equivalent circuits and adding the external components in the usual way gives:
It may help to make a minor redraw of this circuit as follows:
[ Note that ro in the transistor equivalent circuit has been ignored ]
r
E1
B1
ib1
βib1
C1
vRE
iRE
vi1
+
-
vπ
RE
r
E2
B2
ib2
βib2
C2
vi2
+
-
vπ
RC
vo
Q1
Q2
Electronic Circuits and Systems EEE211

## Slide 16
E1
βib1
C1
vRE
iRE
r
B1
ib1
vi1
+
-
vπ
RE
E2
βib2
C2
RC
vo
r
B2
ib2
vi2
+
-
vπ
For a common mode signal, the signal input voltages vi1 and vi2 are considered to be supplied from single common mode source vi. The total current drawn from it is then ib1 + ib2 = ii
Common Mode input resistance
E1
βib1
C1
vRE
iRE
r
B1
ib1
RE
E2
βib2
C2
RC
vo
r
B2
ib2
vi
+
-
vπ
ii
Electronic Circuits and Systems EEE211

## Slide 17
E1
βib1
C1
vRE
iRE
r
B1
ib1
RE
E2
βib2
C2
RC
vo
r
B2
ib2
vi
+
-
vπ
ii
Electronic Circuits and Systems EEE211

## Slide 18
if 2(1+β)RE >> r so the input signal is dropped almost entirely across RE
Hence we need RE to be large for low common mode gain.
We will see later how this can be achieved using a ‘current mirror’ circuit
The common mode voltage gain is calculated as follows:
(Note that only the collector current through Q2 flows through RC)
Common Mode voltage gain
E1
βib1
C1
vRE
iRE
r
B1
ib1
RE
E2
βib2
C2
RC
vo
r
B2
ib2
vi
+
-
vπ
ii
iC2
Electronic Circuits and Systems EEE211

## Slide 19
For a differential mode signal, vi1 = - vi2. and ib1 = - ib2 . The total current through RE does not change because the increase in βib1 is cancelled by an equal decrease in βib2. Hence the potential of point P does not change.
It is now clear by inspection that the differential mode input resistance
Hence a low ICQ would be chosen to achieve a high input resistance. The 741 op amp uses an ICQ of 10A to achieve a differential input resistance of  1 M with β  200.
Differential Mode input resistance
E
βib1
C1
vRE
iRE
r
B1
ib1
vi1
+
-
vπ
RE
E
βib2
C2
RC
vo
r
B2
ib2
vi2
+
-
vπ
P
Electronic Circuits and Systems EEE211

## Slide 20
A differential mode voltage vi1 – vi2 = vi is applied such that vi1  + vi/2 and vi2  - vi/2
Note that this is half that for a normal CE transistor amplifier because in this circuit the input signal is shared equally between two transistors rather than just one for the CE. Only the share of the input signal that is applied to Q2 affects the output current through RC
Differential Mode voltage gain
E
βib1
C1
vRE
iRE
r
B1
ib1
vi1
+
-
vπ
RE
E
βib2
C2
RC
vo
r
B2
ib2
vi2
+
-
vπ
P
Because an equal - but opposite - input signal is applied to the base of each transistor, the potential of point P remains at its DC value. Therefore point P behaves as though it were an ac ground.
Then
Electronic Circuits and Systems EEE211

## Slide 21
Summary – the long tailed pair
0V
R
C
v
i1
Q1
Q2
I
o
R
E
v
i2
v
o
+VCC
-VEE
0V
0V
0V
Common mode
Input resistance
Voltage gain
Differential mode
Input resistance
Voltage gain
For small common mode voltage gain, we need RE large
Conclusions:
For large differential mode voltage gain we need RCICQ large (but limited by VCC)
For large common mode input impedance we need RE large and β large
For large differential mode input impedance we need ICQ small and β large
Common Mode Rejection Ratio
Electronic Circuits and Systems EEE211

## Slide 22: Electronic Circuits and Systems EEE211
Part 3:
Differential Amplifier Design for Performance

## Slide 23
Summary – the long tailed pair
0V
R
C
v
i1
Q1
Q2
I
o
R
E
v
i2
v
o
+VCC
-VEE
0V
0V
0V
Common mode
Input resistance
Voltage gain
Differential mode
Input resistance
Voltage gain
For small common mode voltage gain, we need RE large
Conclusions:
For large differential mode voltage gain we need RCICQ large (but limited by VCC)
For large common mode input impedance we need RE large and β large
For large differential mode input impedance we need ICQ small and β large
Common Mode Rejection Ratio
Electronic Circuits and Systems EEE211

## Slide 24
Note that a large β will increase both the common mode and differential mode input impedances.
So a good design would make RE large, RClCQ large and β large
1. super gain transistors
β1
β2
3. Use FET input transistors instead of bipolar (see next lecture – current mirror)
JFET MOSFET
ri ~ 108  ri ~ 1010 - 1015 
We can make β large by using either:
Very narrow base transistors – typically  ~ 5,000
For IC = 1A, rπ = /gm = 5,000/40 x 1A = 125 M
2. a pair of transistors on the input connected as a ‘Darlington pair’
Effectively:  1 x 2
rπ  (1 2 )/gm giving a large increase in input resistance
Electronic Circuits and Systems EEE211
1

## Slide 25
Differential Amplifier with Constant Current Source Biasing
We have seen that a high RE is required for a low common mode gain (high CMMR)
The very best solution would be to replace RE with a constant current source (remember - a perfect current source has an infinite output resistance).
Question – refer to the summary for a long tailed pair and write down equations for ri(CM) , AV(CM) , r(DM) and Av(DM) in this case.
vi1
R
c
R
c
+V
cc
-V
EE
0V
I
o
vi2
Electronic Circuits and Systems EEE211
2

## Slide 26
The output characteristics of a transistor are a good approximation to a constant current source, so in practice a good solution is to replace RE with a transistor.
R1 and R2 form a potential divider so the voltage on the base of the transistor is
Therefore IE is
so ICQ can be set.
( assuming IB ~ 0 )
A simple example is shown below:
RC
IE1
IE2
Vi1 = 0
IB1
T1
T2
Vi2 = 0
IB2
+VCC
-VEE
RS1
RS2
RE
VB
Io
IE
R2
R1
(Note this is the voltage measured from 0v)
Electronic Circuits and Systems EEE211
3
Current sink circuit

## Slide 27
The dynamic output resistance Ro of this circuit is very high. A small signal analysis shows that Ro is > 10 ro typically, where ro is the output resistance of a transistor. Why is it larger than ro ?
Consider a slight increase in voltage at P. This implies a very slight increase in IO (due to the Early effect) and hence IE. The increase in IE causes a slight increase in the potential of the emitter and hence a slight reduction in VBE which in turn tends to oppose the original increase in IO. That is to say, the resistor RE provides ‘feedback’ that acts to prevent IO rising
R
1
R
2
R
E
VB
Io
P
IE
Therefore the output resistance of the circuit appears larger than just ro
We have seen this before when analysing the output resistance of the CE-ED amplifier.
Electronic Circuits and Systems EEE211

## Slide 28
Reminder – from a previous lecture on CE-ED Output resistance
Assume RS << rπ. Then inject a small current io into the collector terminal. This will cause a small increase in vo
But vπ= - io (rπ//RE)
So the effective resistance from collector to emitter is even larger than ro
rb
r
E
B
gm
vπ
C
vo
ro
B’
RC
io
RE
RL
ib
v
S
RS
R
vπ
i1
if gmro>>1,
Ro
Electronic Circuits and Systems EEE211

## Slide 29
r
E
B
gm
vπ
C
R
ro
io
RE
v
vo
ib
i1
ve
vce
For this circuit, there is a change from the previous CE-ED analysis because there is now a base resistance R = R1//R2 to consider that is in series with rπ.
So what is the output resistance of this current source circuit when a base resistance R is included?
The same method is used to calculate the output resistance. Imagine injecting a small current io into the output and calculate the corresponding vo.
But
Electronic Circuits and Systems EEE211

## Slide 30
Also, if RE >> rπ + R
( In practice it is often not possible to make RE large enough for this condition to be satisfied, so the output resistance will not usually achieve this maximum figure )
r
E
B
gm
vπ
C
R
ro
io
RE
v
vo
ib
i1
ve
vce
Normally,
so
Electronic Circuits and Systems EEE211

## Slide 31: Electronic Circuits and Systems EEE211
Part 4:
Exercise

## Slide 32
Exercises
Q1) Show that the input resistance of the amplifier in figure 1 is given by:-
and that the voltage gain is:-
1
ri’
Electronic Circuits and Systems EEE211

## Slide 33
Q2). The amplifier in figure 2 has one of its inputs grounded. Show that the input resistance for the input signal applied to the remaining input is
where re = r/(1+β)  1/gm
and that the voltage gain is
Show that these reduce to:-
ri  2r and vo/vs  gm Rc/2
and state the necessary approximations.
2
0v
Electronic Circuits and Systems EEE211

## Slide 34
Exercise solutions
Q1) Show that the input resistance of the amplifier in figure 1 is given by:-
and that the voltage gain is:-
a)
b)
Solution
ib
r
E
B
βib=gmvπ
C
RE
vi
ri’
v0
vπ
a)
b)
1
ri’
Electronic Circuits and Systems EEE211

## Slide 35
Q2). The amplifier in figure 2 has one of its inputs grounded. Show that the input resistance for the input signal applied to the remaining input is
where re = r/(1+β)  1/gm
and that the voltage gain is
Show that these reduce to:-
ri  2r and vo/vs  gm Rc/2
and state the necessary approximations.
2
0v
Electronic Circuits and Systems EEE211

## Slide 36
Consider the second transistor. Replacing the transistor with its equivalent circuit and neglecting ro gives:
r
E
B
C
iC
v
vO
RC
gmvπ
iO
r
E
B
C
iC
v
vO
RC
gmvπ
iO
Q2 Solution
Electronic Circuits and Systems EEE211

## Slide 37
Now connect this as a load on the first transistor
re
This has already been analysed in Q1, for which
where now re = ri’
Hence
Electronic Circuits and Systems EEE211

## Slide 38
In this lecture we have:
Analysed the ‘long tailed pair’ differential amplifier circuit to determine its common mode and differential input impedances and common mode and differential voltage gains.
Introduced the concept of a differential amplifier
Identified ‘common mode’ and ‘differential’ voltage gains
Introduced the common mode rejection ratio (CMRR)
Analysed the basic ‘long tailed pair’ differential amplifier circuit to determine its D.C. biasing condition
Electronic Circuits and Systems EEE211

## Slide 39
In next lecture, we will study the current mirror circuit, and how to improve the performance of differential amplifier using C.M..