## Slide 1: Electronic Circuits and Systems EEE211
Current Mirror Circuits
Dept. of Electrical & Electronic Engineering
XJTLU

## Slide 2: Electronic Circuits and Systems EEE211
Part 1:
Current Repeater Circuit

## Slide 3
The current mirror circuit
Notice that the VBE1 = VBE2 (= VBE) and so provided the transistors are identical, the collector currents will be the same also (IC1 = IC2 = IO) .
Hence
This is a very useful circuit to create a temperature compensated current source. It is widely used in integrated circuit designs, because all the transistors are produced at the same time in the same piece of silicon – hence it easy to produce matched transistors that also share the same thermal environment. These are key requirements for the circuit to operate effectively.
V
BE1
I
ref
V
cc
R
V
BE2
I
o
T2
T1
IB
IB
I
o
if β is large
Electronic Circuits and Systems EEE211

## Slide 4
Thus Iref is set by choosing R and this current is then ‘mirrored’ in T2 to provide IO.
Note that if the temperature of the transistors were to change, the VBE of both transistors will change slightly. However, this makes very little change to the total voltage across Rref and so Iref stays almost constant. T1 adopts whatever VBE is needed at the new temperature to keep Iref constant. Since the VBE of T1 is also the VBE of T2, the ‘mirrored’ current IO will also hardly change.
A development of this circuit is the current repeater circuit in which a number of identical current sources can be produced to provide bias currents to different parts of the circuit, as required.
Electronic Circuits and Systems EEE211

## Slide 5
The current repeater circuit
In this circuit, the reference current also feeds all the transistor base currents, so
The reference transistor is placed alongside a series of transistors with their base-emitter junctions connected in parallel.
-vEE
I
ref
V
cc
R
output 1
I
o
I
o
I
o
output 2
output N
VBE
A limitation of this circuit is that the same current is produced in each load, but usually different bias currents will be required. It is possible to scale the currents - within limits - by scaling up the area of the (otherwise identical) transistors:
so
or
Electronic Circuits and Systems EEE211

## Slide 6: Electronic Circuits and Systems EEE211
Part 2:
Widlar Current Mirror

## Slide 7
The Widlar current mirror
It is particularly useful in internal integrated circuit biasing arrangements because:
V
BE1
I
ref
V
cc
R
V
BE2
I
o
= I
c2
I
c1
R
o
R
E
T1
T2
A variation of the basic current mirror circuit can be used if larger current ratios are needed.
a range of currents can be produced by changing the value of RE rather than the size of the output transistor,
the resistance values required are much smaller.
Both of these features leads to a much more compact design.
Electronic Circuits and Systems EEE211

## Slide 8
Analysis
Ignoring base currents so that IE ≈ IC = Io and assuming the transistors are of equal size, then:
hence
but
V
BE1
I
ref
V
cc
R
V
BE2
I
o
= I
c2
I
c1
R
o
R
E
T1
T2
and
This equation allows the required value for RE to be calculated given Iref and the required output current Io.
Electronic Circuits and Systems EEE211

## Slide 9
a.c. Analysis continued – output resistance, Ro
The output resistance Ro ‘seen looking into’ the collector of T2 will depend on the impedance in its base circuit. It is therefore necessary to first determine the resistance represented by the reference circuit (Ro’).
R
R’o
R
g
m1
vπ
rO
B
C
E
r
v
collector connected to base
R’o
Evidently, the output resistance is R // ro // r // (the impedance of the current source)
However, unlike previous analyses, the current source in this case is dependent on the voltage across it through v and so its resistance is not infinite as would be expected for a normal current source.
Electronic Circuits and Systems EEE211

## Slide 10
To determine its effective resistance, imagine injecting a small current i as shown. The resulting small change in v gives the circuit’s effective resistance as v / i.
This is the equation for two resistors in parallel: r1 and the effective resistance of the current source, re1
g
m1
vπ1
B
E
r1
v1
Rog
i
v
ir1
So the total resistance represented by the reference current circuit is
Electronic Circuits and Systems EEE211

## Slide 11
Incorporating this into the second part of the circuit gives:
Finally, if we make rπ2 >> re1 + RE then
We have already analysed this circuit in the last lecture (output resistance of a constant current source with base bias resistors, lecture 4 pp. 24, CE-ED output Resistance)).
In the present circuit, the equivalent base resistance R ≈ 1/gm1 = re1 so the equation becomes:
Eqn (1)
RE
i1
ro2
gm2v
B
r2
E
v
Ro’ ≈ re1
IO
C
T1
Electronic Circuits and Systems EEE211

## Slide 12
Finally, recall the assumption rπ2 >> re1 + RE has been made in this analysis.
In practice, matched transistors of equal area are used in this circuit, so IC2 will be less than IC1 because of the presence of RE. Hence this approximation will be valid for any pair of matched transistors with a reasonable gain.
This implies that rπ2 >> re1 i.e.
Note that
where RE Io is the voltage drop across RE. But VT = 0.025V so only a small voltage is required across RE to ‘multiply up’ the transistor output resistance ro2 and give a large Ro for the current source.
So the output resistance of the Widlar circuit is a factor of 1+gmRE times higher than that of the simple two transistor current source.
or
Electronic Circuits and Systems EEE211

## Slide 13
Example
For the circuit shown, find values for R and RE to give a bias current of Io = 0.1 mA if Iref = 5mA.
Estimate the output resistance, given that both transistors have current gain β = 200 and VA = -110 V. The transistors are of equal size.
Solution
VCC = 5v
VEE = -5v
RE
R
Io
T1
T2
Iref
Rout
So with Io = 0.1mA, and Iref = 5mA, then RE = 978Ω ~ 1k Ω
For matched transistors of equal size, the output current Io is related to Iref through:
Iref = (VCC-VEE -VBE)/R
5x10-3 = (5-(-5) -0.6)/R gives R = 1880 Ω
From KVL applied to the reference transistor:
Electronic Circuits and Systems EEE211

## Slide 14
Assuming that the average collector voltage of T2 will be ≈ 0 volts (so VCE ≈ 5v), the output resistance ro of the transistor is:
The output resistance of the Widlar circuit is therefore:
if rπ2 >> re1+RE
For Io = 0.1mA, gm2 = 40 x 10-4 = 4mA/V
[ Check:-
Hence for RE = 1kΩ ,
Note that a larger RE would be needed if a higher output resistance was required – but check the inequality remains valid and if not, use the full equation for RO (eqn1).
VCC = 5v
VEE = -5v
RE
R
Io
T1
T2
Iref
Rout
Hence the approximation rπ2 >> re1+RE is valid ]
and RE = 1kΩ
Electronic Circuits and Systems EEE211

## Slide 15: Electronic Circuits and Systems EEE211
Part 3:
Differential Amplifier with Active Loads

## Slide 16
Differential amplifier with active loads
0V
R
C
v
i1
Q1
Q2
I
S
R
E
v
i2
v
o
+VCC
-VEE
0V
0V
0V
(1) For low common mode voltage gain, we need RE large
(3) For high differential mode voltage gain we need RCICQ large (but limited by VCC)
(2) For high common mode input impedance we need RE large and β large
(4) For high differential mode input impedance we need ICQ small and β large
We have seen that
We have seen that replacing RE with the high output impedance of a current mirror allows requirements (1) and (2) to be met with reasonable voltage supplies.
Can we do the same with RC to meet (3) and (4)?
Electronic Circuits and Systems EEE211

## Slide 17
The direct approach would be to replace the collector resistor RC by a current mirror in the manner shown in the figure. (note the use of pnp transistors)
Unfortunately this would be very difficult to get to work because the current through T2 is being set by two independent current sources that are in series with each other, i.e. IS and the current mirror T3/T4.
If Iref is not exactly equal to IS/2 then transistor T2 will be driven either hard on or hard off trying to match the two currents.
vi1
T1
I
S
T2
IC1
T4
IC4
+VCC
R
Iref
T3
IC2
-VEE
vi2
vo
This can be solved if any difference in current was allowed to flow as an output current ( IO ). But if IC4 is not equal to IC2 then there will be a DC output current.
Electronic Circuits and Systems EEE211

## Slide 18
1) The reference current Iref through T3 is now IC1 which, with no input signal applied, will be equal to IC2 (because IS shares equally between the two matched transistors T1 and T2). Hence there is no need to match the two separate current sources (IC4 and IC2 ) – it happens automatically and the DC output current of the balanced circuit is zero.
This has a number of advantages:
The solution is to connect the reference transistor T3 into the collector circuit of T1.
2) It doubles the gain of the circuit. If a differential signal voltage is applied so that vi1 increases and vi2 decreases, then IC1 increases and IC2 decreases and the circuit becomes unbalanced. But the increase in IC1 causes the same increase in IC4 due to the action of the current mirror and an output current Iout = IC4 – IC2 is created which is twice that produced by the previous circuit in which IC4 remained constant.
vi1
T1
I
S
T2
IC1
T4
+VCC
T3
IC2
-VEE
vi2
vo
Iout = IC4 – IC2
IC4
Electronic Circuits and Systems EEE211

## Slide 19
Voltage gain
To create an output voltage, the output current must flow though a load resistance RL. In practice this could be the effective input resistance of the next stage. With RL connected, the differential voltage gain from this circuit becomes:
The combined action of T3 and T4 is described as an ‘active load’ (as opposed to a ‘passive load’ RC)
The configuration is a transconductance amplifier with gain
.[Note that this amplifier produces a current output in response to a differential voltage input – i.e. it is a transconductance amplifier.]
Electronic Circuits and Systems EEE211

## Slide 20
The design of a differential amplifier with active loads is the subject of the second piece of experimental work for this module in week 13.
Note:
With the differential input voltage defined as vi1 – vi2, there is no signal inversion – i.e. a positive value for vi1 – vi2 results in a positive output current (and output voltage).
The use of an active load reduces the available voltage swing on the output by the VCE(sat) of T4 but this is not major concern unless the design requires use of very low supply voltages.
In practice, the transistors T2 and T4 will each have a finite output resistance ro so the voltage gain will be:
AV(DM) = gm (ro2 // ro4 // RL ) so to achieve a high gain, RL should be large.
The input impedance of the circuit connected to the output will have a significant effect on the voltage gain of this differential amplifier.
Electronic Circuits and Systems EEE211

## Slide 21: Electronic Circuits and Systems EEE211
Part 4:
Exercises on Current Mirror

## Slide 22
Exercise 1
It is proposed instead to use the circuit in the figure below, in which the transistors are identical.
Show that:
where VT is the ‘thermal voltage’. Assume negligible base currents.
If Ir = 1 mA select values for R, R1 and R2 to achieve Io = 10 A. Resistor values should be less than 50 k. Assume VT = 25 mV.
Electronic Circuits and Systems EEE211

## Slide 23
Exercise 1 solution
To show that:
Assume negligible base currents.
T1
T2
Electronic Circuits and Systems EEE211

## Slide 24
Exercise 1 solution (continued)
If Ir = 1 mA select values for R, R1 and R2 to achieve Io = 10 A. Resistor values should be less than 50 k. Assume VT = 25 mV.
R = (10 – 0.25 – 0.7)/10-3 = 9kΩ
This is the difference in the volt drops across R1 and R2, with that across R1 being larger than that across R2
Choose the volt drop across R1 to be approx twice this value, i.e. 0.25V say.
This gives R1 = 0.25/10-3 = 250Ω and R2 = (0.25 - 0.115)/10-5 = 13.5k
T1
T2
=10V
Electronic Circuits and Systems EEE211

## Slide 25
Exercise 2: Differential amplifier with active load
Show that without RL connected, AV(DM) can be expressed in terms of the Early voltages for T2 and T4 (VAn, VAp respectively ) as:
and state the assumptions made.
The output resistance of T2 = -VAn/IC.
The output resistance of T4 = -VAp/IC.
Without RL,
AV(DM) = gm (ro2 // ro4 ) = gm (VAn/IC // VAp/IC)
Solution
Assumptions made: 300ºK, VCE<<VA
Electronic Circuits and Systems EEE211

## Slide 26
Consider the circuit in the left figure, with transistor parameters ,, and . Determine the input resistance of differential mode - and the common mode input resistance - .

## Slide 29
Electronic Circuits and Systems EEE211
Generally, there are two basic amplifier design technologies: the bipolar technology, which uses npn and pnp bipolar junction transistors; and the MOS
technology, which uses NMOS and PMOS field-effect transistors. We showed that
bipolar transistors have a larger transconductance than MOSFETs biased at the same current levels, and that, in general, bipolar amplifiers have larger voltage gains. We also showed that MOSFET circuits have an essentially infinite input impedance at low frequencies, which implies a zero input bias current.
These advantages of the two technologies can be exploited by combining bipolar and MOS transistors in the same integrated circuit. The technology is called BiCMOS.
BiCMOS technology is especially useful in digital circuit design, but also
has applications in analog circuits.

## Slide 30
Electronic Circuits and Systems EEE211
A basic BiCMOS differential amplifier, with a constant-current source bias and a bipolar active load, is shown in the figure left. Again, the primary advantages are the infinite input resistance and the zero input bias current.
One disadvantage of a MOSFET input stage is a relatively high offset voltage compared to that of a bipolar input circuit. Offset voltages occur when the differential-pair input transistors are
mismatched. (be discussed later)

## Slide 31
Electronic Circuits and Systems EEE211
Multi-Stage Circuit Analysis & Design
Stage 1 is the bias reference section of a current mirror formed with Q2 and Q9
Stage 2 is a differential amplifier with active load that provides voltage gain.
Stage 3 is an emitter-follower circuit forming an impedance matching buffer between stages 2 and 4
Stage 4 is a common emitter amplifier with current mirror load that contributes significantly to the overall
voltage gain..
Stage 5 is a common collector amplifier forming a low/medium impedance output.

## Slide 32
Electronic Circuits and Systems EEE211
Multi-Stage Circuit Analysis & Design – Q1
1) If , make reasonable approximations to estimate the total current drawn by the circuit from the DC voltage supply when the amplifier is biased so that the DC value of and the ac input signals are zero.

## Slide 33
Electronic Circuits and Systems EEE211
Multi-Stage Circuit Analysis & Design – Q1

## Slide 34
Electronic Circuits and Systems EEE211
2) Assuming that the voltage gains of the two common collector stage 3 and 5 are both unity, and reasonable approximations are made to estimate the overall small signal voltage gain of the amplifier, , where:
Assume that all the transistors have a current gain of 100 and an Early voltage of

## Slide 35
Electronic Circuits and Systems EEE211

## Slide 36
Electronic Circuits and Systems EEE211

## Slide 37
Electronic Circuits and Systems EEE211

## Slide 38
In this lecture we have seen:
How the current mirror circuit is able to create a temperature compensated current source and how the basic circuit can be easily adapted to provide a number of separate sources with a range of output currents.
How the range of currents produced by the basic current repeater circuit can be extended with the Widlar circuit without the need for large value resistors, making it particularly suitable for use in integrated circuits.
How the performance of the basic long-tailed pair differential amplifier circuit can be improved by replacing the emitter resistor (the ‘tail’) with a current mirror.
How an active load can be used to produce a high gain differential transconductance amplifier.
Electronic Circuits and Systems EEE211