## Slide 1: Electronic Circuits and Systems EEE211
Introduction to
Feedback (反馈)
Dept. of Electrical & Electronic Engineering
XJTLU

## Slide 2: Electronic Circuits and Systems EEE211
Part 1:
Feedback Structure

## Slide 3: Electronic Circuits and Systems EEE211
Flush toilet (from Wikipedia)

## Slide 4: Electronic Circuits and Systems EEE211
Human Hand vs Robot Hand

## Slide 5: Electronic Circuits and Systems
Ride a bike

## Slide 6: Electronic Circuits and Systems
Feedback System

## Slide 7: Electronic Circuits and Systems EEE211
Introduction to Feedback
In this module we are concerned with electronic systems. However, much of what is covered in this topic are general principles that are equally applicable to other feedback systems – e.g pneumatic and hydraulic control systems etc.
Consider the block diagram of a (negative) feedback system
x
g
x
in
x
f
x
o
A
ol
b
Feedback path
Forward path of signal
+
-
NB arrows indicate the direction of signal flow - NOT current !
We use “x” because it represents a ‘signal’ of some description, (but in our case it will be either a voltage or a current).
Note also that AOL and β can transform a signal from one type into another so the signal can be changed as it passes through different parts of the system. e.g. x0 may be a voltage whilst xg, xf and xin are currents, whilst in a control system, xo might be displacement and xg, xf and xin a voltage.

## Slide 8: Electronic Circuits and Systems EEE211
Feedback network with a feedback fraction β
High gain amp with open loop gain Aol
Input “summer”
Symbols used

## Slide 9: Electronic Circuits and Systems EEE211
Analysis – derivation of the feedback equation
‘open loop’ gain
1
=
+
=
\
OL
OL
g
o
ACL
A
A
x
x
b
‘loop gain’ = βAOL
‘closed loop’ gain
x
g
x
in
x
f
x
o
A
ol
b
+
-
NB. This is the classic equation of feedback theory. Note carefully the terminology used to refer to the various parts of this equation.
(Note – negative feedback will be assumed here)
‘feedback factor’ = 1+βAOL
‘feedback fraction’ β

## Slide 10: Electronic Circuits and Systems EEE211
Note that the loop being referred to is the feedback loop
x
g
x
in
x
f
x
o
A
ol
b
+
-
If the loop is broken (anywhere) then the gain given by simply going round the loop once = ‘loop gain’ = -βAOL Note the negative sign is because it is negative feedback
In practice, it is important that the bias conditions on the amplifier etc are not disturbed when the loop is broken. Some corrective action may be needed to compensate this.
The closed loop gain is the gain of the whole system when the loop is closed = ACL
The open loop gain is the gain of the system when the loop is open (i.e. no with feedback applied) = AOL

## Slide 11: Electronic Circuits and Systems EEE211
If we were to make the loop gain very large (compared to 1), then:
1

+
=
OL
OL
ACL
A
A
b
1
b
and the closed loop gain ACL becomes independent of the open loop gain AOL
This is a very important result,
It means that the overall system gain is no longer dependent on the precision with which the gain of the amplifier A can be made. Just make it large (so that βAOL>> 1, remembering that β is a fraction that usually lies between 10-3 and 1), and the overall gain will instead be set by the feedback fraction β. This often just involves choosing some resistors that can be tightly controlled quite easily – and adjusted if desired.
Note that the gain is reduced by the feedback factor ,1+βAOL (remember – reduced, because this is negative feedback). This quantity is given its special name because it occurs so frequently in feedback theory – it is this same factor by which almost every property of AOL is changed e.g. input and output impedances as well as bandwidth. – as we shall see !

## Slide 12: Electronic Circuits and Systems EEE211
Part 2:
The Effect of Feedback
on Circuits’ Sensitivity and Bandwidth

## Slide 13: Electronic Circuits and Systems EEE211
The sensitivity of ACL to AOL can be quantified by differentiating the feedback equation:
So a given fractional change in AOL is attenuated by the feedback factor to give the resultant fractional change on ACL.

## Slide 14: Electronic Circuits and Systems EEE211
Example
Suppose
Then
If AOL were now to increase by 10% to 1100 then
i.e. an increase of only 0.18 %
Check
The percentage change in ACL should reduce by the feedback factor i.e
The important point to remember is that a change in AOL has a significantly diminished effect on ACL when negative feedback is present – and by a factor given by the feedback factor.
(The minor discrepancy is due to the fact that the 10% change is not a small incremental change, but quite a large one. Better agreement will be obtained if an average feedback factor of 53 were used.)

## Slide 15: Electronic Circuits and Systems EEE211
The Effect of Feedback on Bandwidth
If we now consider an amplifier with bandwidth fO,
Then
where
Log AV
Log f
fOL
AO
AOL ~ 1/f
fCL

## Slide 16: Electronic Circuits and Systems EEE211
Part 3:
Feedback Topologies

## Slide 17: Electronic Circuits and Systems EEE211
x
g
x
in
x
f
x
o
A
OL
b
+
-
In our case, xf, xg and xin (taken as a group) could be either voltage or current and so can xo. Any transformation between the two types of signal would be performed by AOL and β
There are therefore four possibilities to consider:
xg, xf and xin | xo | xO/xg | Amplifier type
voltage | voltage |  | voltage amplifier
current | voltage |  | transresistance amplifier
voltage | current |  | transconductance amplifier
current | current |  | current amplifier
Types of amplifier
‘resistance’ because it is voltage/current, ‘trans’ because it is output voltage and input current (likewise for transconductance)

## Slide 18: Electronic Circuits and Systems EEE211
We can understand a constant voltage source fairly easily because we use them almost every day of our lives.
The source keeps its output terminal voltage constant regardless of the current drawn from it. But it does not necessarily stay constant with time. Examples of sources that try to meet the definition of a constant voltage source would be a car battery and the ac mains.
Pause for thought !!
We will now begin to describe the behaviour of the system with reference to ‘constant voltage’ and ‘constant current’ sources.
But what exactly is a ‘constant voltage’ source and ‘constant current’ source?
Current I
Voltage V
VS
A constant voltage source keeps the voltage constant at VS regardless of the current drawn from it. It’s output resistance is zero
A practical voltage source will not quite achieve the ideal behaviour. It will have an upper current limit and its output resistance will be a small but finite value
Rint = - slope = RO
Rint = - slope = 0

## Slide 19: Electronic Circuits and Systems EEE211
In contrast, a constant current source is very rare in every day life (can you think of an example?) – but very common in electronic systems. A transistor, for example, approximates well to a constant current source)
A constant current source keeps the current constant at IS regardless of the voltage required to force it through the load. Its output resistance is infinitely large
Current I
Voltage V
VS
IS
Note that this is a very different ‘animal’ to the constant voltage source! In no way can the characteristic of a perfect constant current source be regarded as even an approximation to that of a perfect constant voltage source.
As with the constant voltage source, it does not have to stay constant in time – it only has to remain constant with respect to the demands placed on it by the load.

## Slide 20: Electronic Circuits and Systems EEE211
But note that a real source is neither a perfect voltage or perfect current source (although it can come very close to one or the other) and can instead be regarded as either a degraded voltage source or a degraded current source. Hence the duality between a Thevenin equivalent circuit and a Norton equivalent circuit.
I
V
VS
IS
Real source characteristic, source resistance = RS = - slope
RS
VO
VS
Thevenin
RS
VO
IS
Norton
Armed with that review, we now continue the discussion of amplifier behaviour …..

## Slide 21: Electronic Circuits and Systems EEE211
The feedback signal may sense either the output voltage or the output current. The action of negative feedback is to try to keep the sensed signal – whatever it is - constant. (NB. not necessarily in time, but with respect to the load or changes to AOL)
To the extent that it is successful, the output will therefore approximate to either a constant voltage source (if the output voltage is sensed) or a constant current source (if the output current is sensed)
Feedback sensing
The output impedance of the closed loop amplifier will be changed from that of the open loop amplifier – again by the feedback factor.
The amplifier output impedance will be reduced from that of the open loop amplifier roOL to that of the closed loop amplifier roCL = roOL/(1+βAOL) when negative feedback is applied that uses output voltage sensing (which tries to keep vO constant).
Voltage sensing
The amplifier output impedance will be increased from that of the open loop amplifier roOL to that of the closed loop amplifier roCL = roOL(1+βAOL) when negative feedback is applied that uses output current sensing, (which tries to keep iO constant).
Current sensing

## Slide 22: Electronic Circuits and Systems EEE211
To sense the output current, the feedback signal must be obtained from a connection made in series with the output – (often by simply taking the voltage developed across a suitable resistor connected in series with the output signal as shown here).
The series connection increases the output impedance
A
OL
b
iO
to load
To sense the output voltage, the feedback signal will need to be obtained from a connection made across the output - i.e. a shunt connection.
The shunt connection reduces the output impedance.
A
OL
b
vO
to load
Unfortunately, it is not always obvious which sensing arrangement a particular circuit is using! The rule to remember is that if it is voltage sensing the feedback signal should be derived from across the output – if it isn’t, then it will be current sensing !
Practical implementation

## Slide 23: Electronic Circuits and Systems EEE211
A
OL
b
vin
Now look at how the feedback signal can be applied at the input
Since we want negative feedback, the feedback signal must be applied in such a way that it subtracts from the input signal from the signal generator
Again there are two ways this can be done – either as a current or a voltage. Which way is chosen affects the resulting input impedance ‘seen’ by the signal generator.
vg
vf
For the same input current, the input generator now has to supply a larger voltage than it would if there was no feedback signal (vf + vin instead of just vin). The input impedance ‘seen’ by the generator, riCL is therefore increased from riOL to riOL(1+βAOL) by virtue of the series applied feedback. Note the appearance once again of the feedback factor !
i
Feedback application
With this arrangement, the feedback signal is applied in series with the input generator. For this to work the feedback signal must be a voltage and it must subtract from the input voltage (remember - it’s negative feedback).
Voltage feedback

## Slide 24: Electronic Circuits and Systems EEE211
With this arrangement, the feedback signal is applied across the input generator. i.e. a shunt connection. For this to work the feedback signal must be a current that subtracts from the input current (it’s negative feedback).
iin
ig
A
OL
b
vg
if
For the same input voltage, the input generator now has to supply more current with the feedback applied than it would if there was no feedback signal (if + iin instead of just iin). The input impedance ‘seen’ by the generator, riCL is therefore reduced from riOL to riOL/(1+βAOL) by virtue of the feedback.
Current feedback

## Slide 25: Electronic Circuits and Systems EEE211
We next look at some ideal amplifier specifications. You just need to remember:
1. If you choose to use a series feedback connection at the input or output of the amplifier, the relevant impedance is increased.
There is no need to remember the individual equations – it’s just the relevant open loop impedance divided or multiplied by the feedback factor as appropriate.
Ideal amplifier configurations
2. If you choose to use a shunt feedback connection at the input or output of the amplifier, the relevant impedance is decreased.

## Slide 26: Electronic Circuits and Systems EEE211
The feedback signal may sense either the output voltage or the output current. The action of negative feedback is to try to keep the sensed signal – whatever it is - constant. (NB. not necessarily in time, but with respect to the load or changes to AOL)
To the extent that it is successful, the output will therefore approximate to either a constant voltage source (if the output voltage is sensed) or a constant current source (if the output current is sensed)
Review of Feedback sensing
Note that the input impedance, output impedance , gain and bandwidth are all changed from those of the open loop amplifier by the feedback factor.
Negative feedback will reduce the gain and increase the bandwidth from that of the open loop amplifier - by the feedback factor.
series applied feedback will increase the input resistance, shunt applied feedback will reduce the input resistance - in each case by the feedback factor.
series derived feedback will increase the output resistance , shunt derived feedback will reduce the output resistance - again, in each case by the feedback factor)

## Slide 27
In this lecture we have seen:
How to organize feedback system, and knowledge of feedback elements –feedback fraction, loop gain, feedback factor.
Feedback sensitivity and its analysis, calculation comparison.
Feedback topology for different types of configuration.
Electronic Circuits and Systems EEE211