## Slide 1: Electronic Circuits and Systems EEE211
Feedback Application to Amplifiers 1
Dept. of Electrical & Electronic Engineering
XJTLU

## Slide 2: Electronic Circuits and Systems EEE211
Part 1: Ideal Amplifier Configurations

## Slide 3: Electronic Circuits and Systems EEE211
We next look at some ideal amplifier specifications and decide which feedback configuration we will need to use to create them. You need to remember:
1. If you choose to use a series feedback connection at the input or output of the amplifier, the relevant impedance is increased.
Ideal amplifier configurations
2. If you choose to use a shunt feedback connection at the input or output of the amplifier, the relevant impedance is decreased.
We now use this to create four different types of amplifier:
A voltage amplifier
A current amplifier
A transresistance amplifier
A transconductance amplifier
xi
xO
A

## Slide 4: Electronic Circuits and Systems EEE211
1) The voltage amplifier
vL
Amplifier equivalent circuit
vO=Avvi
vi
RS
vS
ri
rO
RL
Consider first the case of a typical voltage amplifier
So for this case, the voltage developed across the load will be dependent not only on its nominal voltage gain but also on:
1) the output resistance of the signal source
2) the resistance of the load to which it is attached
Typical voltage source

## Slide 5: Electronic Circuits and Systems EEE211
The ideal voltage amplifier
So to produce a good voltage amplifier, we want a series feedback connection at the input to make a high input impedance and a shunt connection at the output to make a low output impedance.
To achieve this, we need to make ri >> RS and rO << RL . Then,
But an ideal voltage amplifier should have a voltage gain that is independent of the source and load resistance values
vL
Amplifier equivalent circuit
vO=Avvi
vi
RS
vS
ri
rO
RL
In the limit, an ideal voltage amplifier would have:
i.e. a voltage amplifier would need a SERIES-SHUNT feedback configuration

## Slide 6: Electronic Circuits and Systems EEE211
2) The current amplifier
So to make this into an ideal current amplifier we need ri << RS and rO >>RL so that:
independent of the values of RS and RL
Now consider the case of a typical current amplifier
vL
Amplifier equivalent circuit
iO=Aiii
RS
iS
ri
rO
RL
ii
iL
Typical current source
So to produce a good current amplifier, we need a shunt feedback connection at the input to make a low input impedance and a series connection at the output to make a high output impedance
i.e. a SHUNT-SERIES feedback configuration

## Slide 7: Electronic Circuits and Systems EEE211
3) The ideal transresistance amplifier
ii
vO
Ar
Applying the same principles as in the previous two cases results in the conclusion that to produce a good transresistance amplifier, we need a SHUNT-SHUNT feedback configuration so that:
(also can be described as a current to voltage converter or a current dependent voltage source)
vO
Amplifier equivalent circuit
Ar ii
ii
RS
iS
ri
rO
RL

## Slide 8: Electronic Circuits and Systems EEE211
4) The ideal transconductance amplifier
vi
iO
Ag
To produce a good transconductance amplifier, we need a SERIES-SERIES feedback configuration so that:
iO
Amplifier equivalent circuit
Ag vi
vi
ri
rO
RL
Rg
vg
(also can be described as a voltage to current converter or a voltage dependent current source)

## Slide 9: Electronic Circuits and Systems EEE211

## Slide 10: Electronic Circuits and Systems EEE211
Summary
 | Ideal voltage amplifier | Ideal current amplifier | Ideal trans-conductance amplifier | Ideal Trans-resistance amplifier
Input resistance | infinite | zero | infinite | zero
Output resistance | zero | infinite | infinite | zero

## Slide 11: Electronic Circuits and Systems EEE211
Amplifier type | A | Feedback configuration | rI(CL) | rO(CL)
Voltage amplifier |  | series-shunt |  | 
Current amplifier |  | shunt-series |  | 
Transresistance amplifier |  | shunt-shunt |  | 
Transconductance amplifier |  | series-series |  | 
For the practical case, feedback is used to approximate the ideal amplifier

## Slide 12: Electronic Circuits and Systems EEE211
Part 2: Identification of Feedback Topologies on Discrete Circuits

## Slide 13: Electronic Circuits and Systems EEE211
To sense the output current, the feedback signal must be obtained from a connection made in series with the output – (often by simply taking the voltage developed across a suitable resistor connected in series with the output signal as shown here).
The series connection increases the output impedance
A
OL
b
iO
to load
To sense the output voltage, the feedback signal will need to be obtained from a connection made across the output - i.e. a shunt connection.
The shunt connection reduces the output impedance.
A
OL
b
vO
to load
Unfortunately, it is not always obvious which sensing arrangement a particular circuit is using! The rule to remember is that if it is voltage sensing the feedback signal should be derived from across the output – if it isn’t, then it will be current sensing !
Practical implementation Lecture 7. 22

## Slide 14: Electronic Circuits and Systems EEE211
Some practical examples
Output voltage sensing
In this example, the feedback signal is being taken from the collector of a common emitter amplifier as a shunt connection
There is a direct connection to the output voltage terminal so it is clearly sensing the output voltage. It is therefore SHUNT derived feedback.
The output impedance will be reduced by the feedback (shunt connection)
vo
RC
VCC
0 v
RL
RE
Feedback to input
CC

## Slide 15: Electronic Circuits and Systems EEE211
Output current sensing
In this example the output voltage is being taken from across an un-bypassed emitter resistor but the feedback is taken from across a collector resistor in series with RE.
There is no direct connection to the output voltage – so the feedback must be sensing the current and is SERIES derived.
The feedback is SERIES derived so the output impedance will be increased by the feedback
The feedback acts to keep iC constant (the feedback signal is monitoring icRc)
RC
VCC
0 v
RL
RE
vo
Feedback to input
iO
iC

## Slide 16: Electronic Circuits and Systems EEE211
With this arrangement, the feedback signal is applied across the input generator. i.e. a shunt connection. For this to work the feedback signal must be a current that subtracts from the input current (it’s negative feedback).
iin
ig
A
OL
b
vg
if
For the same input voltage, the input generator now has to supply more current with the feedback applied than it would if there was no feedback signal (if + iin instead of just iin). The input impedance ‘seen’ by the generator, riCL is therefore reduced from riOL to riOL/(1+βAOL) by virtue of the feedback.
Current feedback Lecture 7. 24

## Slide 17: Electronic Circuits and Systems EEE211
Input current summing
So the current into the amplifier is increased by the feedback.
This feedback is a shunt connection. It forms a node at which the currents sum.
Kirchoff’s current law gives:
Feedback from output
RC
VCC
CE
RE
iO
ii
RS
vS
iS
if
The input impedance will therefore be reduced by this SHUNT applied feedback connection.
or

## Slide 18: Electronic Circuits and Systems EEE211
A
OL
b
vin
Now look at how the feedback signal can be applied at the input
Since we want negative feedback, the feedback signal must be applied in such a way that it subtracts from the input signal from the signal generator
Again there are two ways this can be done – either as a current or a voltage. Which way is chosen affects the resulting input impedance ‘seen’ by the signal generator.
vg
vf
For the same input current, the input generator now has to supply a larger voltage than it would if there was no feedback signal (vf + vin instead of just vin). The input impedance ‘seen’ by the generator, riCL is therefore increased from riOL to riOL(1+βAOL) by virtue of the series applied feedback. Note the appearance once again of the feedback factor !
i
Feedback application Lecture 7. 23
With this arrangement, the feedback signal is applied in series with the input generator. For this to work the feedback signal must be a voltage and it must subtract from the input voltage (remember - it’s negative feedback).
Voltage feedback

## Slide 19: Electronic Circuits and Systems EEE211
Input voltage summing
Again, the signal voltage into the amplifier is being reduced by the feedback - as is required for the feedback to be negative. An increase in the base voltage causes the feedback signal to increase the emitter voltage also, therefore the feedback is trying to keep the net voltage across the emitter-base junction constant.
The input impedance will be increased by this SERIES applied feedback connection.
Assuming the source impedance is small compared to the input impedance of the stage, then:
In this example, there is no direct connection to the source, so it must be a series connection.
Feedback from output
RC
VCC
RE
vi
~vS
RS
vS
vf
a)

## Slide 20: Electronic Circuits and Systems EEE211
Input voltage summing
Again, the signal voltage into the stage is reduced by the negative feedback.
The input impedance will be increased by this series feedback connection. A voltage increase of vS results in a voltage increase of vf (and hence also an increase of the emitter potential at point P) via the feedback loop. The input impedance ‘seen’ by vS is therefore increased.
The second example requires a differential input stage. Note again there is no direct connection to the source. In this case it is clearly a series connection giving a difference signal as a consequence of the differential input stage
b)
Feedback from output
RC
VCC
~vS
RS
vS
vf
P

## Slide 21: Electronic Circuits and Systems EEE211
Example circuit 1
1) feedback topology?
3) Effect on:
4) Amplifier type?
the gain ?
ri ?
ro?
2) feedback type?
series(indirect connect) - Shunt(Direct connect)
ac and DC negative feedback
reduced
decreased
increased
A voltage amplifier
100mV
4.7k
vOUT
VCC = 10V
2N2222
2k
100
10k
6.8
Vg
2N2222
100
10k
4.7k
Q1
Q2
Q3
2N2907A
10k
10k
Rb1
Rb2
Rg
RC1
R1
C1
Rf2
Rf1
RL
-VEE = -10 V
10k
RC

## Slide 22: Electronic Circuits and Systems EEE211
Vg
1mV
Rg
750
2.2u
C1
Q1
Re1
3.9k
C3
82u
i
in
Q2N2222
Rc1
Q2
Q2N2907A
Re2
2k
Ce2
6.8u
Vcc
Q2N2222
Q3
Rc2
6.2k
Rc3
3.48k
i
out
Vee
Re3
6.2k
C2
1u
v
out
RL
1k
Rf 26.1k
Feedback resistor
12V
12V
Vcc
Vcc
Vee
Vee
+
+
-
-
4.7k
if
1) What is the feedback topology of the circuit shown?
2) What Is the type of feedback?
3) What (qualitative) effect would you expect the feedback to have on:
4) What is the best description for type of amplifier?
the overall gain of the amplifier?
the input impedance
the output impedance?
Shunt(Direct connect)-series(indirect connect)
ac and DC negative feedback
Reduced
A current amplifier
Example circuit 2
Increased
Decreased

## Slide 23: Electronic Circuits and Systems EEE211
v
g
+VCC
5.1kΩ
12kΩ
10kΩ
4.7kΩ
4.7kΩ
0V
1kΩ
0V
Rf = 100kΩ
vo
Q1
Q3
Q2
if
iS
ii
1) feedback topology?
3) Effect on:
4) Amplifier type?
the gain ?
ri ?
ro?
Shunt(Direct connect)- Shunt(Direct connect)
reduced
A transresistance amplifier
2) feedback type ?
negative ac and DC feedback
Example circuit 3
decreased
decreased

## Slide 24: Electronic Circuits and Systems EEE211
Example circuit 4
1) feedback topology?
3) Effect on:
4) Amplifier type?
the gain ?
ri ?
ro?
2) feedback type?
Vg
vOUT
VCC= 10V
2N2222
220k
600
2.2k
1k
1.2k
Q1
Q2
2N2907A
RE2
Rf
VEE= -10V
1F
9.1k
11k
15k
series(indirect connect) - series(indirect connect)
reduced
A transconductance amplifier
negative ac and DC feedback
increased
increased

## Slide 25: Electronic Circuits and Systems EEE211
Advantages of Negative Feedback
1. Negative feedback reduces the sensitivity of the gain on parameters of an amplifier such as transistor current gain etc.
2. Negative feedback allows us to set gain to any value we want (up to the limit of AOL).
3. Negative feedback increases the bandwidth of the amplifier.
4. Negative feedback reduces distortion
5. Negative feedback allows us to adjust the input and output impedances of an amplifier.
BUT these advantages do not come FREE!
Disadvantages of Negative Feedback
1. Negative feedback always reduces the gain of an amplifier.
2. Over certain frequency ranges, it can be that negative feedback changes from negative to positive with catastrophic results. Positive feedback increases the gain of the amplifier and the amplifier could then oscillate – no longer any use as an amplifier
MUST REMEMBER THESE!

## Slide 26
In this lecture we have seen:
Four types of Feedback topology analysis.
Actual circuit are analyzed.
Electronic Circuits and Systems EEE211