## Slide 1: Electronic Circuits and Systems EEE211
Operational Amplifiers
Dept. of Electrical & Electronic Engineering
XJTLU

## Slide 2: Electronic Circuits and Systems EEE211
Part 1: Introduction

## Slide 3: Electronic Circuits and Systems EEE211
Operational Amplifiers
Specially designed to be used with feedback. Originally op-amps used to perform mathematical operations – additional, subtraction, differential and integration – then put together to build analogue computers – which could solve differential equations, etc.
1st Op – amps used valves! – then transistors – then integrated circuits
1st successful op-amp was μA741 introduced in 1968
WHY are OP - AMPS so important?
We found that for an amp. with feedback, the closed loop gain was
If loop gain >>1 then ACL ~1/β
So to build a precision amplifier (i.e. one with a precise gain) it is sufficient to just buy a few precision resistors and a cheap, low precision but high gain op-amp.
The transition from valves to transistors occurred around mid 1960’s

## Slide 4: Electronic Circuits and Systems EE211
741 has open loop gain of 2 X 105 or 200V output per 1mV input
Some op-amps can have gains as high as 107 or ~ 10V / µV
Review of Basics
Non-inverting input Vout = Av Vp
Inverting input Vout = - Av Vn
Vout = Av (Vp - Vn)

## Slide 5: Electronic Circuits and Systems EE211
Omitting power supplies, equivalent circuit is
The output voltage source is controlled by the differential input voltage vd
so if there is no load, vO = AOLvd
For 741
i.e. looks like a reasonable voltage amplifier
But a perfect voltage amplifier has infinite input impedance, zero output impedance and finite but well defined voltage gain
An operational amplifier has large input impedance, low output impedance and very high but poorly-defined voltage gain

## Slide 6: Electronic Circuits and Systems EEE211
Part 2: Basic Operational Amplifier Circuits and Analogue Computer

## Slide 7: Electronic Circuits and Systems EEE211
Basic Op-amp Circuits
1. Non-inverting amplifier circuit
NB this is an op-amp circuit- not just an op-amp but also has feedback resistors
Replacing the op-amp by its equivalent circuit gives
How do we calculate vO/vg ?
- Use nodal analysis

## Slide 8: Electronic Circuits and Systems EEE211
The voltage gain analysis will be greatly simplified if we make the approximation that the op-amp is a perfect voltage amplifier
i.e. ri → ∞ and rO → 0.
(because there is no current into the non-inverting input)
(because there is no current into the inverting input)
Solving gives:
where
2
1
vp
vn
4
3
vp = v2 = vg
For node 2
For node 3
vo = v4 =AOL(vp – vn)
For node 4
If the loop gain is high, then

## Slide 9: Electronic Circuits and Systems EEE211
The Virtual Short Principle
An Op – amp has a very high gain, so for any reasonable output voltage, the differential input voltage vp – vn will be vanishingly small
So if the gain is very large then we can say that vp – vn ~ 0, or vp ~ vn
This is a very useful approximation – a ‘Golden Rule’ !!
( But remember – it only applies if the gain is very large)
So an op-amp outputs a voltage that keeps the voltage that feeds back to the inverting input practically the same as the voltage on the non-inverting input
We say that vn tracks vp
This leads to the concept of a virtual short – the circuit behaves as though there is a short across the inputs because the voltage difference between vp and vn is kept zero, but it is not actually shorted . Hence the name ‘Virtual short’. It greatly simplifies the analysis of op-amp circuits.

## Slide 10: Electronic Circuits and Systems EEE211
1 The non-inverting amplifier
( from Virtual short principle )
Lever analogy
input
output
L1
L2
Examples of op-amp circuit analysis using Virtual Short Principle
0V

## Slide 11: Electronic Circuits and Systems EEE211
2. Inverting amplifier
Note that R1 could include (or be entirely represented by) the output resistance of the signal source. e.g the output impedance of a strain gauge bridge as will be discussed in the Instrumentation module.
From the virtual short principle, vn  vp = 0V
Then
Lever analogy
input
output
L1
L2
0V

## Slide 12: Electronic Circuits and Systems EEE211
3. The summing amplifier
This example has 3 inputs, but could be as many as you want
Since vn = 0 (from virtual short principle) , KCL gives
N.B. the sources don’t interact – e.g. if one input is changed, the currents from the other inputs are not affected
So the output voltage is equal to the sum of all the inputs with each multiplied by an individual gain factor set by Rf and R1, R2 and R3

## Slide 13: Electronic Circuits and Systems EEE211
4. The difference amplifier
Has 2 inputs, 1 output
Use superposition:
[ vg2 is turned down to zero, leaving only its internal resistance in the circuit (= 0 for a perfect voltage source) ]
Contribution to vO due to vg2 alone is
So
gives
So to make a difference amplifier we require
giving
[We shall see later it is even better if R1 = R3 and R2 = R4 to minimise the offset voltage]
Then contribution to vO due to vg1 alone is
Now restore Vg2 and turn Vg1 down to zero instead, leaving only its internal resistance (0) in the circuit.

## Slide 14: Electronic Circuits and Systems EEE211
5. The differentiator
KCL gives
i.e. Output is proportional to the time derivative of the input
6. The integrator
i.e. Output is proportional to the time integral of the input
KCL gives

## Slide 15: Electronic Circuits and Systems EEE211
A practical application – the Analogue Computer
Widely used in the 1960’s before the digital revolution – still found in some special applications
Suppose we want to solve the differential equation
Then
So we need an integrator and a summing amplifier
'Weighted’ summer

## Slide 16: Electronic Circuits and Systems EEE211
Circuit Design
as required

## Slide 17: Electronic Circuits and Systems EEE211
Part 3: Input and Output Resistances of Common Operational Amplifiers Circuits with Feedback

## Slide 18: Electronic Circuits and Systems EEE211
Input and output resistances of common feedback amplifiers
1. Input Resistance of the Non Inverting Amp (shunt derived, series applied feedback)
We can write:
iin
vin
iin
vin
So the input resistance is rd(1+βAOL) in series with the resistance to ground from the inverting input.
The solution of these equations gives:
And assuming that there is no load connected – i.e. RL =0, then
Replacing the op-amp with its equivalent circuit gives
Note that usually rO << R2 so:

## Slide 19: Electronic Circuits and Systems EEE211
Note also that often R1//R2 << rd[1+βAOL] so
So the effective input resistance ‘seen’ by the source is increased from rd to
as a result of the series applied feedback
An understanding of why this happens can be obtained as follows (ignoring ro):
If the input voltage is vp then the feedback makes vn equal to:
(which is usually only very slightly less than vp)
So feedback makes the actual voltage drop across rd much smaller than vp alone
vn= βvO
vp
iin
Rin
i.e.

## Slide 20: Electronic Circuits and Systems EEE211
Output Resistance
To determine Ro, turn the input down to zero and imagine a test voltage vt applied across the output terminals. Find the current it and hence the output resistance = vt/it
Solving gives
So output resistance is reduced by the feedback factor 1 + βAol when shunt derived feedback is used
vt
it
if rd >> R1and rO << R1
+
R
2
R
1
-
i
t
R
out
+
v
t

## Slide 21: Electronic Circuits and Systems EEE211
The reason for this can be understood as follows:
and therefore
So this time the feedback makes the actual voltage drop across ro much larger than vt alone and the resistance therefore appears much smaller than it really is.
AOLβv1
it
Rout
vt
ro
so the volt drop across ro is then
vt
it
If vt increases, then vn increases by βvt and the voltage output from the op-amp reduces by AOLβv1
so

## Slide 22: Electronic Circuits and Systems EEE211
We can use the same method to obtain expressions for Rin and Rout for an inverting amplifier.
(Recall that the feedback topology is associated with a transresistance amplifier – so do you expect Rin and Rout to be large or small?).
Input Resistance of Inverting Amp (shunt derived, shunt applied feedback)
The input resistance of the feedback amplifier is defined at the summing node, as shown below.
Rin
R1
R2
+
ro
vS
rd
v
o
- AvOLvi
ii
vd
Rin

## Slide 23: Electronic Circuits and Systems EEE211
Looking into the summing node assuming ro <<R2 and noting that vd = ird.rd then:
R1
R2
+
ro
vS
rd
v
o
- AvOLvd
ii
vd
Rin
Note that Rin is the original input resistance of the open loop amplifier rd reduced a shunt connected resistance R2/(1+AvOL). We have seen this before - the Miller effect
e.g. If AvOL = 105, rd = 1MΩ and R2 = 10kΩ, R1 = 1kΩ (i.e. a closed loop voltage gain of 10);
Then Rin = 0.1Ω which is small - as expected!

## Slide 24: Electronic Circuits and Systems EEE211
Note:
We can also express Rin in terms of the transresistance gain by noting that:
Therefore from the previous equation for Rin:
For the previous example: AvOL = 105, rd = 1MΩ and R2 = 10k, R1 = 1k, then ArOL =rd AvOL = 106 x 105 = 1011 V/A and βr = 1/104 Ω-1 so Rin = 106/(1+10-4 x 1011) ≈ 0.1Ω - as before.
Noting that βr = iR2/vo =1/R2 then
if AvOL >> 1
So the input resistance of the open loop transresistance amplifier has been reduced by the transresistance feedback factor as expected.

## Slide 25: Electronic Circuits and Systems EEE211
The source ‘sees’ an input impedance R’in = R1 + Rin =1kΩ + 0.1Ω ~ 1kΩ
That is, the input resistance of the amplifier seen by the source voltage is effectively equal to R1
So when designing a circuit of this type, choose R1 to meet the required input resistance and then choose R2 to meet the required voltage gain (-R2/R1)
Rin
Note:
R’in
1) The transresistance amplifier has almost zero input resistance (i.e. Rin ≈0) and so in this circuit it is fed by a current equal to vg/R1
Therefore the output voltage is
vo = iin x ArCL = iin x ArOL /(1+βr ArOL)≈ iin x 1 /βr = - vg/R1 x R2= -vg x R2/R1
- which is the familiar equation for this amplifier circuit

## Slide 26: Electronic Circuits and Systems EEE211
Part 4: Finding Loop Gain

## Slide 27: Electronic Circuits and Systems EEE211
Finding the loop gain
We have seen that the feedback factor (1+βA) is a very important quantity that determines the small signal behaviour of a feedback amplifier in many ways.
To determine its effect in a given amplifier it is necessary to calculate the loop gain βA. This can be done as follows:
1) Suppress xg (turn it down to zero)
2) Break the feedback loop at some convenient point
Imagine injecting a test signal xt
4) Trace round the loop to find return signal xr
+
-
AOL
b
x
g
x
o
x
i
x
f
“loop”
Then
+
-
x
g
= 0
AOL
x
r
x
t
Break
Test signal
-
b
AOL
x
t
AOL
x
t
b
b
AOL
x
t
Note
it should be negative, (otherwise the feedback is positive!)
It doesn’t matter where in loop break is made (but it is best done after a generator)
and the Loop gain is

## Slide 28: Electronic Circuits and Systems EEE211
Example 1 Find the loop gain for the non-inverting amplifier
(not a very good op-amp!)
Consider the non-inverting amplifier below and suppose
Then, calculate the return signal vr:
Note that had an ideal amplifier been assumed,
Break the loop and insert a test signal, vt
+
v
d
+
-
r
d
62k
2.7k
AOL v
d
v
r
+
v
t
r
o
Then loop gain =
+
v
t
v
r
Aol v
d
+
r
o
= 1k
62k
2.7k
r
d
10k
v
d
NB. Polarity !!
vn
vp

## Slide 29: Electronic Circuits and Systems EEE211
(Compared to the approximate value 1/β =0.0417-1= 24)
and
W
=
=
5
.
234
264
.
4
1
k
+
@
1
|βAOL|
r
R
o
o
- big! (as required for a V-amp)
- small! (as required for a V-amp)
Note that if the gain had been AOL = 2 x 105 , rd = 2MΩ, ro = 75Ω, (typical values for 741 op-amp) then repeating the analysis gives
βAOL = 8.35x103 and

## Slide 30: Electronic Circuits and Systems EEE211
Op-amp has
So feedback is negative and the loop gain is
741
v
g
-
v
o
+
+
1k
10k
R’
in
R
in
Example 2 Find the loop gain for the inverting amplifier
(a transresistance amplifier)
1k
10k
r
d
-
+
ro
Break
+
vn
vp
vr
vt
ArOLird
1k
10k
r
d
-
+
ro
Break
+
ArOLird
vn
vp
ird

## Slide 31: Electronic Circuits and Systems EEE211
- Small - as expected – shunt derived
- Small - as expected (because the feedback is shunt applied)
i.e. Rin is set by the external resistor !