## Slide 1: Electronic Circuits and Systems EEE211
Operational Amplifiers Continued…
Dept. of Electrical & Electronic Engineering
XJTLU

## Slide 2: Electronic Circuits and Systems EEE211
Part 1: The Effect of Negative Feedback on Amplifier

## Slide 3: Electronic Circuits and Systems EEE211
The effect of negative feedback on distortion
Distortion occurs when the output is not a magnified but otherwise exact copy of input.
Compare the open loop and closed loop Voltage Transfer Curves (VTC) of an amplifier .
v
o
v
in
+Vcc
-VDD
Slope of the transfer curve in this region is the value of AOL quoted by the manufacturer
AOL
ACL
Real amplifiers are only approximately linear because:
Provided the open loop gain is large enough for βAOL >>1 then the closed loop gain is determined by 1/β and is independent of AOL. So distortion is reduced (by the feedback factor)
Negative feedback reduces distortion - why?
2) Output voltage swing is limited to approx. +/- VCC
1) Transistors are not very linear devices

## Slide 4: Electronic Circuits and Systems EEE211
Another common example – ‘cross-over’ distortion
Consider the very common ‘push-pull’ circuit shown below
This is a small signal amplifier (the op-amp stage) followed by a ‘push-pull’ output stage that is two common collector (CC) stages in series across the power supply. (Note the supply voltage is balanced about ground). Because of the current gain of the CC amplifier, it is able to provide high power to the load (e.g. a loudspeaker)

## Slide 5: Electronic Circuits and Systems EEE211
During one half cycle Q1 is OFF and Q2 is ON
During the following half cycle Q1 is ON and Q2 is OFF
etc
During the period of ‘cross-over’ between these two transistors conducting, there will be a short period when neither transistor conducts, which occurs whilst the input voltage to the base of the transistors changes from -0.7 to + 0.7 volts.
This causes “Cross-over” Distortion” So the output waveform becomes

## Slide 6: Electronic Circuits and Systems EEE211
One solution is to (carefully) bias both the transistors slightly ON so that there is only a very small voltage change required on the base of the transistors to make them start conducting significantly.
BUT an alternative and highly effective method is to include the push-pull circuit within feedback loop, giving :
The cross-over distortion is eliminated in the output waveform because the op-amp produces whatever output is necessary to make vn = vp. Since vn is linearly related to vo through the feedback fraction, vo will also have a linear relationship to vg

## Slide 7: Electronic Circuits and Systems EEE211
The output jumps between levels -0.7V to +0.7V to force the push pull amplifier through its “dead band” quickly. In effect, the input to the push-pull stage is pre-distorted by the op-amp in order to compensate for the distortion produced by the push-pull.
This occurs because the feedback is monitoring the output voltage at the load rather than the output of the op-amp itself and so the amplifier maintains 1/β = vo/vg rather than 1/β = voa/vg
voa
vo
vo
voa

## Slide 8: Electronic Circuits and Systems EEE211
Effect of Negative Feedback on Amplifier Bandwidth
The frequency response of transistor amplifiers is determined by CAPACITORS – either internal to the transistor itself or in the external circuit.
The frequency response is specified with reference to the bandwidth of the amplifier, defined as the difference between the frequencies at which the gain has fallen by 3dB from its maximum (mid-band) value. (3dB because the power - which is proportional to V2 -is halved)
Note that this is a log – log graph (the vertical axis is plotted in dB)
Useful “BANDWIDTH”
f
Lo
f
Hi
Log f
Voltage Gain in dB
Low Frequency
Region
Mid Frequency region
High Frequency
Region
Gain falls at low frequencies because of coupling and emitter resistance by-pass capacitors - i.e capacitances external to the transistor
AvOL
Gain falls at high frequencies because of capacitances internal to the transistor – i.e Cπ and Cμ
3dB

## Slide 9: Electronic Circuits and Systems EEE211
What happens when we apply feedback? How is bandwidth affected?
We can easily see when these two approximations apply if we plot 1/β on the same graph as AOL
We know that with feedback applied, the gain becomes
when βAOL << 1
when βAOL>> 1

## Slide 10: Electronic Circuits and Systems EEE211
dB
log10 f
f
Lo
f
Hi
0dB
1/β (dB)
AOL (dB)
Note that in this example, β is assumed to be the same at all frequencies
βAOL = 1 where the graphs for AOL and 1/β cross,
f
1
f
2
Region 1
Aβ < 1 up to f1
Region 2
Aβ > 1 between f1 and f2
Region 3
Aβ < 1 beyond f2
So the curve for ACL follows 1/β in region 2 and AOL in regions 1 and 3.
The NEW Bandwidth has been increased by the feedback to f2 – f1

## Slide 11: Electronic Circuits and Systems EEE211
Example
AV0L = 105 = 100 dB
Then
Suppose the op amp in this circuit has an open loop frequency dependence shown above
Bandwidth = 5Hz
so
AOL dB
100 dB
5 Hz
Log10 f
- 20dB/decade
R2 = 99k
R1 = 1k

## Slide 12: Electronic Circuits and Systems EEE211
Adding the plot of 1/β onto the plot of the open loop gain gives
Open loop gain = 105, bandwidth is 5 Hz
Closed loop gain =102, bandwidth = 5 kHz
Gain is reduced by the feedback factor (1+βAOL)  βAOL= 0.01x105 = 103
Bandwidth is increased by the feedback factor = 103
So the Gain x Bandwidth product is constant.
A factor of ten increase in frequency results in a factor of ten reduction in gain. i.e. AOL is proportional to 1/f
1/β = 40dB
AOL
ACL≈ 1/β
ACL≈ AOL
A dB
100dB
5 Hz
Log10 f
- 20dB/decade
5 kHz

## Slide 13: Electronic Circuits and Systems EEE211
Part 2: The Effect of
Bandwidth Limitation on Pulse Response

## Slide 14: Electronic Circuits and Systems EEE211
The effect of bandwidth limitation on pulse response
a) STEP response
Consider the low pass CR circuit, first with a step input and then with a sinusoidal input:
R
C
Vi(t)
VO(t)
where τr = RC is the rise ‘time constant‘ of the circuit
gives
Solution of the circuit equation:
with
ta=0
time
Vo(t)
Vs
ta=0
time
V
i
(
t
)
Vs

## Slide 15: Electronic Circuits and Systems EEE211
b) Sinusoidal response
So the rise time constant of the pulse response is related to the upper corner frequency of the frequency response by:
R
C
Va(t)
VO(t)
where ωH = 1/RC
So we can deduce the upper bandwidth frequency from the time constant of the leading (or trailing) edges of the pulse response and ‘vice versa’.

## Slide 16: Electronic Circuits and Systems EEE211
a) STEP response
Now consider the high pass CR circuit, first with a step input and then with a sinusoidal input:
where τd =RC = droop time constant
gives
Solution of the same circuit equation:
C
R
Vi(t)
VO(t)
But with
ta=0
time
V
i
(
t
)
Va
ta=0
time
‘droop’
Vo(t)
Va

## Slide 17: Electronic Circuits and Systems EEE211
b) Sinusoidal response
So the droop time constant of the pulse response and the lower corner frequency of the frequency response are related by:
where ωL = 1/RC
R
Va(t)
VO(t)
So we can deduce the lower bandwidth frequency from the time constant of the droop along the top edge of the pulse response and ‘vice versa’.

## Slide 18: Electronic Circuits and Systems EEE211
The same consideration applies to the response of any first order system. The upper and lower corner frequencies of the system may be determined from the pulse response and ‘vice versa’.
A (dB)
Log10 f
fL
fH
-20 dB/decade
+20 dB/decade
e.g. an amplifier
Input waveform
Output waveform
time
voltage
Rise time related to high frequency performance (fH)
Droop time related to low frequency performance (fL)

## Slide 19: Electronic Circuits and Systems EEE211
Note:
It is common practice to determine the ‘10% – 90%’ rise time of a transient. This allows comparison with systems for which the transient is not exponential and for which the concept of a ‘time constant’  would therefore not be appropriate.
For the case of an exponential response the relationship between the ’10 - 90% rise time’ and the ‘time constant’ (note the two different wordings) is:
The 10% level (t = t1) is given by
hence
The ’10 – 90% RISE TIME’ is therefore: tr = t2 – t1 = 2.2 x τ, but only for an exponential response
The 90% level (t = t2) is given by
hence
where RC is the ‘time constant’, τ

## Slide 20: Electronic Circuits and Systems EEE211
Note that this assumes an exponential (1st order) response (but this is sometimes overlooked!).
There is therefore a relationship between the upper cut-of frequency and the 10-90% rise time that is often quoted:
Similarly, the 10 – 90% droop time of the pulse gives the lower cut off frequency of the amplifier (e.g. due to coupling capacitors etc) to be
NOTE: The analysis also assumes that there is negligible interaction between the rise and droop times tr and td . i.e fH >> fL In practice, this assumption is usually valid.

## Slide 21: Electronic Circuits and Systems EEE211
Part 3: Slew Rate

## Slide 22: Electronic Circuits and Systems EEE211
A (dB)
Log10 f
fL
fH
-20 dB/decade
+20 dB/decade
Input waveform
Output waveform
time
voltage
Rise time related to high frequency performance (fH)
Droop time related to low frequency performance (fL)
So the ’10 – 90% RISE TIME’ = 2.2 x τr - but only for an exponential response
1) Bandwidth limitation and pulse response (review of last lecture)

## Slide 23: Electronic Circuits and Systems EEE211
Effect of the ‘slew rate’ limit on amplifier response
e.g. a pulse waveform output would look like (unity gain assumed here):
output
input
time
Voltage
Maximum dv/dt = slew rate
output
input
time
Voltage
Maximum dv/dt = slew rate
and a sinusoidal waveform output would look like:
Op-amps have a limit on how rapidly the output voltage can change that is set by the ‘slew-rate’
( For a 741 op-amp the slew rate is quoted as 1V/μS )

## Slide 24: Electronic Circuits and Systems EEE211
Note that for a first order response, the rise time of a pulse output will become limited by the slew rate limit when maximum dv/dt = slew rate.
output
input
time
Maximum dv/dt = slew rate
τ
For a first order system the maximum rate of change of voltage is given by:
Vm
So the output will become slew rate limited when

## Slide 25: Electronic Circuits and Systems EEE211
Note that to obtain an accurate estimate for the time constant from a pulse measurement, it is important to check that the amplitude of the applied pulse does not cause the slew rate to be exceeded.
The magnitude of the applied pulse must be such that
Example:
Determine the pulse output voltage for which a circuit with bandwidth 10MHz that uses a 741 op-amp becomes slew rate limited.
(slew rate limit for 741 op-amp = 1V/μS),
So set up a pulse and measure τ. Then check that the value obtained satisfies the above eqn.
Expected time constant of the pulse rising edge is:
Therefore the rising edge will become slew rate limited when
Solution

## Slide 26: Electronic Circuits and Systems EEE211
If the input signal is sinusoidal, the slew rate limit is reached when
A slew rate limited output will be apparent from the shape of the output waveform:
Again, unlike the upper bandwidth limit, the frequency at which the slew rate limit is reached depends on the amplitude of the output signal as well as it’s frequency.
So if the slew rate limit is reached, reduce the amplitude of the signal to avoid distortion
Example: What is the maximum frequency at which an undistorted output signal of 10V amplitude can be obtained using a 741 op-amp? (SR = 1V/μsec)
Solution: Vm = the maximum frequency that could be used is obtained from
SR = Vmω = Vm2πfm
input
output
dv/dt limit
Vm
Therefore fm= slew rate/(Vm2π) =106 / 20π ~16kHz. Higher frequency signals will be distorted.

## Slide 27: Electronic Circuits and Systems EEE211
Part 4: The Imperfections of Operational Amplifiers

## Slide 28: Electronic Circuits and Systems EEE211
3) The Offset bias of op-amps
DC imperfections of operational amplifiers include bias current, offset voltage, and offset current. They result in non-zero output voltage even at zero input voltages. This effect is especially noticeable in high gain or precision DC amplifiers.
Here Vp = Vn = 0 (tied to ground) so ideally we expect
However, in practice, we usually find
Suppose an op-amp has both its inputs connected to ground.
a) Offset voltage

## Slide 29: Electronic Circuits and Systems EEE211
We can therefore model this contribution to the output voltage in a practical op-amp by inserting a DC voltage Vos at the input of an ideal op-amp as shown:
The manufacturer usually quotes the magnitude of VOS - eg for 741C, VOS = 2mV typical, 6mV max.
This means ~50% of 741C’s tested have VOS between -2mV to +2mV, but all have VOS between -6mV and +6mV.
The offset voltage Vos is the equivalent input voltage that would need to be applied (as shown) to make VO = 0
N.B. VOS is always (by convention) assumed connected to the non-inverting (+ve) input, with the polarity shown. ( But note that it can be a positive or negative value! )

## Slide 30: Electronic Circuits and Systems EEE211
If the circuit requires these currents to flow through resistances in the external input circuit, then a voltage will be generated that acts as an input voltage to the op-amp - so it is amplified to give a DC output VO.
The input bias currents can flow either in or out of the op-amp depending on whether the input stage is constructed with npn or pnp transistors:
b) Bias currents
These are input currents IBp and IBn that MUST be provided for the operational amplifier to function properly.
If pnp transistors are used, the current flows out of the input terminals.
If npn transistors are used, the current flows into the input terminals.

## Slide 31: Electronic Circuits and Systems EEE211
These currents are particularly troublesome because they are sensitive to temperature – the output voltage drifts
-
+
VO
Vi
R1
R2
R3
For example, in the inverting op-amp circuit, always make R3 = R1//R2 to minimise the effect of the bias currents
c) The Offset current
VO = Av (IBp – IBn) x 1M
+
-
I
Bp
I
Bn
+
-
1
M
v
+
+
-
v
-
1
M
Even if the two bias currents are made to flow through equal resistances at the input, their effects will still not cancel exactly because the bias currents themselves are usually not quite equal in magnitude. The difference between the bias currents is called the offset current IOS = IBp − IBn

## Slide 32: Electronic Circuits and Systems EEE211
The manufacturer, after measuring a large number of samples, gives us the ‘input bias current’ which is the average bias current
‘input offset current’
In the WORST possible case, this means either
or
Summarise this by saying that in all cases
AND they give us the ‘offset bias current’ which is the magnitude of the bias current difference
For a 741C:
max
200
,
20
max
500
,
80
A
n
typical
nA
I
nA
typical
nA
I
os
B
=
=
For example:

## Slide 33: Electronic Circuits and Systems EEE211
v
os
+
-
+
IBp
I = 0
I = 0
Ideal op-amp
(zero offsets)
IBn
So the complete model of the op-amp with both offset voltage and bias currents is:
We can use this model to determine the DC offset voltage that will occur in a given circuit.

## Slide 34: Electronic Circuits and Systems EEE211
For example, the differential amplifier circuit gives:
We can determine the contribution to Vo from each source individually using the ‘principle of superposition’
To determine the contribution due to offset bias alone, assume no input signals are being applied so the two inputs are grounded.
vos
+
-
+
IBp
Ideal op-amp
IBn
VO
R1
R2
R3
R4

## Slide 35: Electronic Circuits and Systems EEE211
The contribution from Vos
vos
+
-
+
IBp
Ideal op-amp
IBn
VO
R1
R2
R3
R4
The contribution from IBp
The contribution from IBn
The total Vo

## Slide 36: Electronic Circuits and Systems EEE211
The total Vo
Note that to find the maximum and minimum possible value of Vo we need to consider carefully the appropriate values to use for the sign of Vos and the values of IBp and IBn
The maximum possible value of Vo will be given by the maximum positive value of Vos, the maximum value of IBp and the minimum value of IBn
The minimum possible value (i.e. the most negative value) of Vo will be given by the maximum negative value of Vos, the minimum value of IBp and the maximum value of IBn

## Slide 37: Electronic Circuits and Systems EEE211
vos
+
-
+
IBp
Ideal op-amp
IBn
VO
R1
R2
R3
R4
If we make the resistance ‘seen’ by IBp equal to that ‘seen’ by IBn , i.e. R3//R4 = R1//R2
Then
and the only contribution from the bias currents will be due to the difference between them , i.e. the offset bias current.
Consider the special case R3//R4 = R1//R2

## Slide 38: Electronic Circuits and Systems EEE211
vos
+
-
+
IBp
Ideal op-amp
IBn
VO
R1
R2
R3
R4
Always make the resistance ‘seen’ by IBp equal to that ‘seen’ by IBn
Remember these are DC currents, so only consider DC paths.
Note:
The remaining contribution to the output voltage:
has to be compensated by an external biasing circuit.
+
-
+VCC
-VCC

## Slide 39: Electronic Circuits and Systems EEE211
Example:
Calculate the maximum range of VO for the amplifier circuit shown with R1 = 45k, R2 = 90k, R3 = 10k
given that:
Most probable value for VO is half way through this range i.e. -30 mV
[Note IBp and IBn will both have the same sign (positive in this example), but can have different magnitudes]
vos
+
-
+
IBp
Ideal op-amp
IBn
VO
R1
R2
R3
From the values for Ios and IB, then
Answer

## Slide 40: Electronic Circuits and Systems EEE211
Most probable value for VO is half way through this range i.e. 0 mV
Note that if we choose R3 = R1//R2 = R = 30kΩ then:
NB Much better than previous case where there was no possibility at all that could be zero.

## Slide 41: Electronic Circuits and Systems EEE211
N.B.
It is important to remember that we are dealing here with DC quantities for VOS and IBp and IBp. The analysis must consider only DC paths. If capacitors are present then the analysis must treat them as OPEN CIRCUIT because they block DC.
So in this circuit we make R3 = R1//R2 so that the DC paths resistances seen be the bias currents IBp and IBn are equal
But in this circuit we make R3 = R2 because the capacitor blocks the DC path through R1
C1