## Slide 1
EEE213 Power Electronics and Electromechanism
Tutorial (lecture 1 to 5)

## Slide 2: Problem 2.1
A single-phase bridge rectifier is required to supply an average voltage of 110V to a resistive load R=10 Ω. The main supply is 220V RMS. Determine
  1)The rms value of the input voltage for the rectifier and then the turns ratio of the transformer;
  2)The voltage and current ratings of the diodes;
  3)The power rating of the transformer;
  4)The power consumed by the load;
  5)The THD of the line current.
Lecture 2

## Slide 3: Problem 2.2
2.2 A battery charger is supplied by a single-phase bridge rectifier. The battery voltage is E=20V and the capacity is 10Ah. The current-limiting resistor is 10ohm. The input voltage is 30V RMS. Draw the waveforms and then calculate
  1)The conduction angle of a diode;
  2)The average charging current;
  3)The charging time;
  4)The power dissipated on R;
  5)The peak reverse voltage across a diode.
Lecture 2

## Slide 4: Problem 3.1
A three-phase bridge rectifier supplies a ripple-free current I0=10A and an average voltage V0=110V to the load.
Assume vA=Vmsinωt.
  1)Determine the rms value of the phase voltage;
  2)Draw the current and voltage waveforms for D1, D3, D5;
  3)Draw the current waveform for phase A and determine the rms value;
  4)Determine the diode ratings.
Lecture 3

## Slide 5: Problem 3.2
The single phase bridge rectifier is supplied from a 120V, 60Hz source. The load resistance is R=500ohm.
  a) Design a capacitive filter so that the ripple factor of the output voltage is less than 5%;
  b) With the value of capacitor C in part a), calculate the average load voltage Vdc.
Lecture 3

## Slide 6: Problem 4.1
A full converter is connected to a 100V-50Hz supply vs. The load is purely resistive with R=10 ohm.
  (1) Draw the waveforms for the output voltage, the current, and the line current for a firing angle .
  (2) Express the line current is in a Fourier series;
  (3) Determine the THD of the line current;
  (4) Determine the displacement power factor cosϕ and the line power factor fP;
  (5) If the firing angle is α = π/3, calculate V0, THD, cosϕ , fP and the power dissipated by the load.
Lecture 4

## Slide 7: Problem 4.2
Repeat the previous question when a very large inductor is put into series with the resistor.
Lecture 4

## Slide 8: Problem 5.1
A three-phase full bridge SCR rectifier supplies a DC power to an RL load. The output current ripple is negligible. The firing angle is 45°.
  Draw the waveforms for the output voltage, the voltage across SCR1, and the line current of phase A.
Lecture 5

## Slide 9: Problem 5.2
A resistive load R=10 in series with a very large inductor is supplied by a bridge rectifier connected to a three-phase power supply with a phase voltage of 100V. It is required to obtain an average voltage of 150V. Calculate
  1)The firing angle needed;
  2)The average current;
  3)The rms output voltage and current;
  4)The power consumed by R;
  5)The average and rms values of a thyristor current;
  6)The rms line current;
  7)The input power factor.
  Draw the waveforms for the output voltage, a thyristor voltage and a line current.
Lecture 5

## Slide 10: Problem 2.1
A single-phase bridge rectifier is required to supply an average voltage of 110V to a resistive load R=10ohm. The mains supply is 220V RMS. Determine
  1)The rms value of the input voltage for the rectifier and then the turns ratio of the transformer;
  2)The voltage and current ratings of the diodes;
  3)The power rating of the transformer;
  4)The power consumed by the load;
  5)The THD of the line current.

## Slide 11: Problem 2.2
A battery charger is supplied by a single-phase bridge rectifier. The battery voltage is E=20V and the capacity is 10Ah. The current-limiting resistor is 10ohm. The input voltage is 30V RMS. Draw the waveforms and then calculate
  1)The conduction angle of a diode;
  2)The average charging current;
  3)The charging time;
  4)The power dissipated on R;
  5)The peak reverse voltage across a diode.

## Slide 12: Problem 2.2
A battery charger is supplied by a single-phase bridge rectifier. The battery voltage is E=20V and the capacity is 10Ah. The current-limiting resistor is 10ohm. The input voltage is 30V RMS. Draw the waveforms and then calculate
  1)The conduction angle of a diode;
  2)The average charging current;
  3)The charging time;
  4)The power dissipated on R;
  5)The peak reverse voltage across a diode.